## Slide 1: PowerPoint 12: PPE
PowerPoint presentation
1. Health and safety in building services engineering
1.12 Types of PPE

## Slide 2: Objectives
At the end of the session the learners should be able to:
  state the purpose of personal protective equipment (PPE) to mitigate risks
  identify the various types of PPE
  understand the correct methods of using PPE.

## Slide 3: PPE
The guidelines that govern protective clothing are set out in the Personal Protective Equipment at Work Regulations 1992. PPE is defined as all equipment designed to be worn or held to protect against a risk to health and safety. PPE includes most types of protective clothing and equipment (eg, eye, ear, hand, foot and head protection). PPE is necessary when you cannot remove the hazard.
PPE does not stop accidents but reduces the effects of an accident.

## Slide 4: PPE
  PPE is designed to protect you against workplace hazards. Your employer is obliged by law to provide the correct PPE. For example:
      protective clothing, overalls, etc
      high-visibility (HI-VIS) wear
      eye protection
      gloves
      safety helmets
      safety footwear
      ear defenders
      dust masks, respirators.

## Slide 5: Head protection
On site there is always the danger of objects falling from overhead, but helmets are also needed to protect against the danger posed by protruding objects. They are designed to protect the head against general bumps. Head protection is a requirement for site work and must be worn correctly and be well fitting. Examples of head protection are a safety helmet or hard hat, and a ‘bump cap’.

## Slide 6: Eye protection
Protection for your eyes comes in many forms for different situations, each specific to the work being carried out. Eye protection shields you from heat, sparks, dust, dirt, flying objects and fumes. The different types of eye protection are:
  safety goggles
  safety visors
  safety spectacles
  face shields
  fixed shields.

## Slide 7: Ear protection
When working in the construction industry, if noise levels reach 85db then ear protection should be worn to avoid damage to the hearing. This noise level can easily be reached when drilling, chasing, sawing or grinding. The type of protection you should use will depend on the work you are doing and the duration of the noise. The commonest types of ear protection are:
  ear defenders
  ear plugs.

## Slide 8: Protective clothing
There are many types of workwear designed for use in different conditions, such as dust, dirt, heat, oil and grease.
Some are even disposable, for use in certain situations. Types include:
  overalls
  safety trousers
  work jumpers
  work uniforms
  elbow protection.

## Slide 9: High-visibility wear
As the name suggests, high-visibility (HI-VIS) clothing comes in bright colours to make the person easy to spot by other workers on site, such as crane operators and the drivers of site trucks. The clothing is typically reflective, for use in darker environments.
High-visibility waistcoats are now a requirement for all site work. However, the following types of HI-VIS PPE are also available:
  safety trousers
  safety jackets.

## Slide 10: Hand protection
Gloves are designed to suit specific types of work and protect the hands from hazards such as sharp objects and hot materials. The types of gloves available include:
  general rigger’s gloves
  arm-length gauntlets
  chemical-resistant gloves
  heat-resistant gloves
  abrasion-resistant gloves
  cut-resistant gloves
  gauntlets
  electrician’s gloves.

## Slide 11: Knee protection
Some trades spend a lot of their working day on their knees (eg plumbers and electricians), and this can cause pain now and arthritis in later life. Knee protection is used to guard against this. For example:
  kneeling mats
  knee pads.

## Slide 12: Foot protection
Good footwear will protect your feet against various hazards, including damp, sharp and heavy objects, chemicals and electricity. Standard site boots will need toe protectors and some sites may require a steel mid-sole to protect the underside of the foot. This combination protects against dropping items on your foot or treading on nails.
The types of foot protection available include:
  safety shoes
  safety boots
  safety trainers.

## Slide 13: Lung protection
When working in the construction industry, dust and fumes are commonly encountered. To overcome these health and safety hazards, RPE (respiratory protective equipment) should be used:
  dust masks
  respirators
  breathing apparatus
  face-fit apparatus.

## Slide 14: Vibration protection
Protection against arm and hand vibration for construction workers is vitally important to ensure that ‘vibration white finger’ (VBW) does not affect the operative. This requirement is covered in the Control of Vibration at Work Regulations 2005 and this document sets out the protection required. Mitigation approaches for VBW include:
  risk controls
  alternative work methods
  equipment selection
  work limitation (vibration exposure)
  gloves.

## Slide 15: Fall protection
When working at height in the construction industry, it is paramount that fall protection measures are put in place to mitigate the likelihood and consequences of a fall from height. For example:
  harnesses
  fall arrest lanyards
  safety nets
  edge protection
  airbag protection.

## Slide 16
Any questions?