## Slide 1: PowerPoint 16: Safety in excavations and confined spaces
PowerPoint presentation
1. Health and safety in building services engineering
1.16 Safe practices and procedures for working in excavations and confined spaces

## Slide 2: Objectives
By the end of the session learners should be able to:
  understand the dangers associated with working in excavations and confined spaces
  describe the safe working practices required when working in excavations and confined spaces.

## Slide 3: Excavations
Working in trenches may be required on construction sites. The danger comes from collapse and falling objects. If you need to work in an excavation, the job must be:
  planned
  risk assessed
  managed
  supervised.
These steps are required to ensure that there is no harm to your health when you are working in an excavation.

## Slide 4: Excavations
There are many situations where you may find yourself working in excavations, including:
  sewers
  foundations
  underground service mains
  drains
  wells
  plant rooms.
Before beginning work in any of these areas, careful planning is required.

## Slide 5: Excavations
All excavations deeper than 1.2m must have their sides supported to ensure they do not collapse.
Other factors to be aware of are:
      type of ground that is being dug
      access and egress
      storage of the spoil dug out of the excavation
      vehicle stops
      second emergency exit ladder
      warning notices
      Excavation sites must have a barrier to ensure nobody falls into the excavation.

## Slide 6: Excavations
When you are digging and excavating, for example, to install an incoming water main, always check the type of ground that is being dug.
  Clay tends to be firmer.
  Sandy soil tends to collapse more easily.
If the ground is soft, the sides of the excavation should be sloped.
Always think: safety first!

## Slide 7: Confined spaces
A confined space is a place which is substantially enclosed (though not always entirely), and where serious injury can occur from hazardous substances or conditions within the space or nearby (eg lack of oxygen).
  Think: health and safety first!
  Can I get out if something goes wrong?
  The safety of personnel is paramount, so a suitable emergency escape route must always be maintained, and communication with people outside the confined space must always be possible.

## Slide 8: Confined spaces
There may be many instances where you will be required to work in a confined space, such as:
  flues
  chimneys
  roof areas
  sewers
  attics
  under suspended floors.
Working in these cramped conditions can be challenging.

## Slide 9: Confined spaces
The dangers associated with working in a confined space are:
      claustrophobia
      lack of oxygen
      build-up of fumes or vapours
      access and egress difficulties
      fire
      explosion
      hot working conditions
      flooding.

## Slide 10: Confined spaces
If you are working under a suspended floor in a domestic property, there will be dangers from:
  becoming trapped
  fire, if soldering
  fumes/vapours
  vermin/insects
  dust
  sharp objects.

## Slide 11: Confined spaces
Before working in a confined space, consider the following:
  Have I been trained?
  Should I be working alone?
  Am I wearing the correct PPE?
  Is there adequate lighting?
  Is there adequate ventilation?
  Am I aware of the situation and associated hazards?
Before you begin, consider whether you can give satisfactory answers to the above questions to ensure the work can be completed safely.

## Slide 12
Any questions?