## Slide 1: PowerPoint 1: International system of units (SI) and derived units
PowerPoint presentation
2. Construction science principles
2.1 International System of Units (SI)
2.2 Derived SI units

## Slide 2: What are SI units?
The units that scientists use all over the world are standardised in the Système Internationale d’Unités: SI units. (There is one exception – North America uses imperial units.) Working in SI units in construction means measurements are consistent and recognised globally.
There are seven base units:
kilogram (kg)
metre (m)
second (s)
ampere (A)
kelvin (K)
mole (mol)
candela (cd).

## Slide 3: SI units in building services engineering
SI unit | Abbreviation | Measures
Kilogram | kg | Mass
Second | s | Time
Hour | h | Time
Kelvin | k | Temperature
Pascal | Pa | Pressure, quantity internal pressure
Bar | bar | Pressure
Joule | J | Energy
Here are the units you are mostly likely to encounter in building services engineering.

## Slide 4: SI units
SI unit | Abbreviation | Measures
Watt | W | Power
Newton | N | Force
Litre | l | Volume
Candela | cd | Luminous intensity
Illuminance | Lux | Illumination
Metre | m | Length

## Slide 5: Derived SI units
Derived units come from the seven base units. For example, a watt is a derived unit.
It is important to be familiar with some common derived SI units:
Area is measured in m2 (eg, a room 10m long x 10m wide = 100m2).
Volume is measured in m3 (eg, a room 10m long x 10m wide x 10m high = 1000m3).
When measuring the rate of flow of a liquid, the units used are litres per second (l/s) and metres cubed per hour (m3/h).
While volume is a measure of 3-D space, when dealing with liquids it is more commonplace to use the term capacity.

## Slide 6: Derived SI units
Density is measured in kilograms per metre cubed (kg/m3).
Specific heat capacity is measured in kJ/kg/ºC.
Velocity is measured in metres per second (m/s).
Acceleration is measured in metres per second squared (m/s2).
When working with electricity, in addition to the base SI unit of amperes (A):
volt (V) is the derived unit for electric potential, electric potential difference (voltage) and electromotive force
ohm (Ω) is the derived unit of electrical resistance
coulomb (C) is the derived unit of electric charge
watt (w) is an SI unit of power used to measure the rate of energy transfer.

## Slide 7: Mass and weight
Mass is the amount of matter in an object and is measured in kilograms. An object cannot have a mass of zero.
Weight is a force due to the pull of gravity on the mass of the object and is measured in newtons (N). Weight = force x gravity’s acceleration.
We often confuse the terms and weight is often quoted in kilograms.
Pressure is defined as force/area. The SI unit for force is newtons (N) and the SI unit for area is square meters (m²). One newton per square metre (N/m²) equals 1 pascal.
Example: when a liquid or a gas is in contact with a solid surface such as water in a tank it produces a force on that surface. The pressure of the fluid is defined as the force per unit area.

## Slide 8: Multiples and sub-multiples
When working with small areas, volumes, distances, or power supplies the units you calculate are comparatively small and therefore not difficult to record.
For example, the UK mains power supply is an alternating current with a frequency of 50 hertz (Hz) and 230 volts (V).
In large engineering projects, the forces, distances, speeds or volumes involved can be much larger, meaning the numbers become inconvenient to record in full. In precision engineering, there will also be very tiny and precise measurements. In engineering notation or engineering form the exponent of 10 must be divisible by 3 (ie powers of a thousand, but written as, for example, 106 instead of 10002).
1,000,000 can be written as 10002 or in engineering form as 106.

## Slide 9: Multiples and sub-multiples
Multiple size | Power of 10 (x10²) | Prefix | Prefix abbreviation
1,000,000,000,000 | 12 | tera- | T
1,000,000,000 | 9 | giga- | G
1,000,000 | 6 | mega- | M
1,000 | 3 | kilo- | k
0.01 | -2 | centi- | c
0.001 | -3 | milli- | m
0.000001 | -6 | micro- | μ
0.000000001 | -9 | nano- | n
Multiples and sub-multiples also allow orders of magnitude to be recorded in shortened form.

## Slide 10: Worked example
The distance from the Sun to Pluto is 4,400,000,000,000m
This can also be written as:
4.4 × 1012m
It can be shortened again with the prefix tera to:
4.4 terametres
Or abbreviated to:
4.4 Tm

## Slide 11: Which is greater?
Which is greater: 230kV or 2.3MV?
230kV is equivalent to 230kV = 230 x 1,000= 230,000V
2.3MV is equivalent to 2.3MV = 2.3 x 1,000,000 = 2,300,000V
So, 2.3 MV is the greater amount.

## Slide 12
Any questions?