## Slide 1: PowerPoint 2: Materials science principles
PowerPoint presentation
2. Construction science principles
2.3 Materials science principles

## Slide 2: Materials: an introduction
PowerPoint presentation
A wide range of materials are used in building design. The choice of material used will depend on its properties.
The principles of materials science are used in building services engineering to ensure buildings perform over time, in terms of durability and stability.
Materials are selected for their suitability for the job they are performing. For example, their durability, weather resistance, heat resistance, water resistance, conductivity or malleability.

## Slide 3: Types of materials
Ferrous and non-ferrous metals.
Alloys and solders.
Plastics (thermosetting and thermoplastic).
Fireclays/ceramics.
Natural and synthetic rubbers.

## Slide 4: Metals
Iron and steel are ferrous metals. Steel is used for structural applications such as portal frames. Magnetic effects only work with ferrous metals.
Non-ferrous metals are rarer and more resistant to corrosion than ferrous metals. They include aluminium, copper and lead.
Copper is a pure metal that is used for water and heating pipework as it doesn’t react with water, ensuring the water remains uncontaminated.

## Slide 5: Alloys
An alloy is a mixture of two or more elements, where at least one element is a metal. Steel is an example of an alloy. Pure iron, for example, is very soft. Adding tungsten to iron makes tool steel, which is harder than pure iron.
Steel | Elements | Properties
Mild steel | Carbon and iron | Can be bent and pulled into wires
Tool steel | Tungsten and iron | Hard, resistant to high temperatures
Stainless steel | Chromium and iron | Hard, resistant to corrosion
Solder is a metal alloy usually made of tin and lead which is melted using a hot iron. It is used to join two metal components together.

## Slide 6: Metals in building services engineering
HVAC systems
Plumbing pipework
Cable trays
Two-core steel wire armoured cable

## Slide 7: Plastics
Thermosetting plastics become rigid when heated and do not soften when reheated. For example, epoxy resins used in anchor bolts.
Thermoplastic is a flexible plastic that becomes pliable and solidifies. It can be recycled. Good examples are guttering and downpipes and electrical insulation on cables.
Cross-linked polyethylene (XLPE) is a form of polyethylene with cross-links. It is used in building services pipework systems, hydronic radiant heating and cooling systems, domestic water piping and insulation for high tension (high voltage) electrical cables. Compared to thermoplastic polyethylene, XLPE does not melt and is thermally resistant, as well as being more resistant to environmental stress.

## Slide 8: Ceramics and fireclays
Ceramics – toilet pans and cisterns are made from ceramics which are coated with a slip which is fired to form an impervious layer. Ceramics are also used on isolators in electrical systems, such as an electric rail line.
Fireclays are a refractory material that is resistant to decomposition by heat, pressure or chemical attack, and retains strength and form at high temperatures. Fire bricks are used for lining furnaces and fireplaces.

## Slide 9: Natural and synthetic rubber
Natural rubber is an elastic substance obtained from the latex sap of rubber trees. It has many industrial uses but today synthetic rubber alternatives are more commonly used instead.
Rubber can be vulcanised to make it resistant to temperature and more durable.
Synthetic rubber is produced using petroleum-based materials. It can be used for flooring material, hoses, seals and other applications of natural rubber.
Silicone is used in sealants or expansion joints due to its waterproof and adhesive qualities.

## Slide 10: Properties of materials
Chemical composition – a term that is often used to define the composition of soils. For example, alkaline soil, where sulphate-resistant cement would have to be specified.
Ductility – the ability of a material to be drawn out under tension without breaking. Gold is an example of a ductile material.
Malleability – the ability of a material to be hammered or rolled into a shape. For example, cold-formed sheeting.
Conductivity – the ability of a material to allow an electrical charge to pass through and along it. Copper wire is highly conductive.

## Slide 11: Properties of materials
Tensile strength – the resistance of a material to being torn apart. For example, a tie in a cavity wall has tensile strength.
Compressive strength – the strength of a material to resist force and weight directly applied to it. For example, a foundation has compressive strength.
Strength – the measure of tensile, shear and compressive forces on a material and its ability to withstand such forces, stresses and strains.
Durability – the useful life of a product in terms of years. For example, brick, stone and steel all have high durability.

## Slide 12: Failure and degradation of materials
Time, ultraviolet (UV) light and weathering from the elements all contribute to the degradation of a material, for example:
  a clay brick will absorb water which freezes in winter and expands, causing damage to the face of the brick
  timber, if untreated, will absorb water and fungus and deteriorate by rotting
  sunlight discolours some plastic materials (eg roof lights) causing them to become brittle and crack.

## Slide 13: Environmental conditions
The integrity of materials can be affected by different environmental conditions.
Oxidation of metals – aluminum, if unprotected, will oxidise in the atmosphere, creating a coating on the surface.
Rust – iron is widely used in building construction and it is important to protect it from rust. Metals such as aluminium, chromium and zinc are higher than iron in what is called the electromotive series (see Slide 15). This means that although they corrode more readily, they produce oxides that form a thin coating which then protects them from further deterioration.

## Slide 14: Environmental conditions
Atmospheric corrosion – acid rain is a primary source of corrosion, caused by sulphur dioxide from burning fossil fuels.
UV and heat damage to plastics – frequent hot summer days can cause plastics to weaken and bend.
Electrolytic corrosion is caused by the action of water. Dissimilar metals (eg copper and aluminium) in the presence of an electrolyte (water) generate an electrical charge which causes corrosion.

## Slide 15: The electromotive series and erosion
In the electromotive series, metals are ordered by their tendency to be oxidised, ie how reactive they are. Lithium is easily oxidised whereas gold is not and is therefore not reactive. This quality can be important for choosing materials which do not corrode easily (eg copper piping).
Finally, the mechanical movement of parts causes a form of corrosion known as erosion corrosion. You may know this as ‘wear and tear’. As moving parts operate, they become worn. Destroying or weakening something gradually in this way is another definition of corrosion.

## Slide 16
Any questions?