## Slide 1: PowerPoint 12: 4.10 Documentation used in construction projects
4: Construction and the built environment industry

## Slide 2: Documents on site
A range of documents are needed for a construction project to run smoothly. These documents are used to ensure clear and accurate transmission of important information between personnel.
In this session we will look at some documents that are used when working on building services engineering tasks.
Note that some of the documents are also used by other trades and construction professionals.

## Slide 3: Document types
Take off sheets. ‘Taking off’ is the process of identifying information and measurements from drawings and documentation during preparation of costings.
An example could be an electrician taking off linear measurements of cable requirements or a plumber taking off lengths and diameters of pipework required.

## Slide 4: Document types (continued)
Contracts. Defined as ‘a promise or set of promises that the law will enforce’. There are a range of contract descriptions such as Design and Build, Construction Management, Measured term, Repair and Maintenance.
Schedule of rates. Lists setting out rates for staff, labour, plant hire, etc. This is an important part of contractual arrangements when the nature of the work cannot be accurately quantified prior to work commencing.

## Slide 5: Document types (continued)
Estimates and quotes. Remember, in session 6, estimates were defined as essentially a ‘best guess’ of how much specific work will cost, or how long it will take to complete.
A quote was defined as a promise to do work at an agreed price which sets out exactly what work will be done for that agreed price.
Delivery notes. This document lists materials and components shipped from a supplier to site. This is an important document that should be checked for accuracy at the time of delivery to avoid discrepancies causing production delays later.

## Slide 6: Document types (continued)
Purchase order. Often referred to as a ‘PO’, a document issued by the buyer to the seller showing which materials and components the contractor wishes to buy. When the supplier accepts the PO, it can become a legal contract document.
Bill of quantities. Created by a quantity surveyor to produce quotes and estimates and other information for the project.
It can include details about the client and architect, descriptions of materials, measured quantities related to each task and details of required components.

## Slide 7: Document types (continued)
Wiring diagrams. Highlights and labels the actual interconnections within the circuit and the supply provisions. Used with layout diagrams to show the route and position of wiring, position of junctions, position of sockets and switches and distribution boards.

## Slide 8: Document types (continued)
Other documents. Keep in mind that there are many more documents used throughout the construction process. Some are referred to as contract documents which are legally binding.

## Slide 9
Any questions?