## Slide 1: PowerPoint 8: Renewable energy and energy conservation
PowerPoint presentation
5.10 Renewable energy and energy conservation

## Slide 2
High-carbon power is electricity produced by fossil fuels, which have high greenhouse gas emissions. Coal is the most carbon intensive, followed by oil and then natural gas. Other generation sources are lower in carbon. Solar PV and geothermal are slightly more carbon intensive than other non-fossil sources, but still very low carbon compared with any fossil fuel.
High carbon
High-carbon examples
Natural gas/ LPG
Fuel oils (coal and peat)

## Slide 3
Low-carbon power is electricity produced with substantially lower greenhouse gas emissions than conventional fossil fuel power generation. The energy transition to low-carbon power is one of the most important actions required to limit climate change.
Low-carbon examples
Combined heat and power (CHP)
Heat pumps
Solid fuel
Solar thermal
Electricity from non renewable resources
Combined cooling heat and power
Low carbon

## Slide 4
When energy sources are labelled carbon-free, this means that energy is produced by a resource that generates no carbon emissions. These resources help to reduce greenhouse gas emissions.
Zero-carbon examples
Electricity – wind
Solar PV
Electricity – tidal
Hydroelectric
Zero carbon

## Slide 5: Rainwater harvesting
In the UK, we rely on mains water to supply all our water needs. Financially and environmentally this is wasteful; hence the rise in rainwater harvesting systems and techniques.
Mains water is purified to drinking water standards and this is an expensive process. Much of our water usage is for non potable purposes such as cleaning, gardening and flushing toilets.
Harvested rainwater can be substituted for mains water, which reduces our reliance on the mains water supply, saves money and protects a key natural resource.

## Slide 6: Rainwater harvesting
In the South East of England there is less water available per person than in most Mediterranean countries.
Rainwater is usually collected from the roof and then is heavily filtered using a filter attached to the downpipe on a guttering system. A fine basket filter may be used in larger, more expensive systems, for example self-cleaning filters can be placed in underground tanks.
The velodrome in the Queen Elizabeth Olympic Park in London is designed to harvest rainwater.

## Slide 7: Rainwater systems
There are three types of rainwater systems available:
Gravity – Collected rainwater is pumped from the main holding tank to an elevated/header tank. The connected appliances are then supplied from the tank as in a normal gravity-fed system.
Direct (pressurised) – Collected rainwater is pump-fed directly from the main holding tank to the serviced appliances.
Combination – Collected rainwater is pumped or gravity fed to a low-level break tank. In turn, the water is then gravity fed to an integral or external booster pump system for onward distribution to the serviced appliances.

## Slide 9: Rainwater harvesting system
Advantages
Disadvantages
It saves money by reducing water usage.
It gains eco home rating for a property.
Rainwater is better for your garden as it has a balanced pH and is free of chemicals such as chlorine.
It has a high cost when retro-fitted to an existing property.
The filter requires maintenance.
Separate pipework needs to be installed.
It can produce drinking water for livestock and for irrigating crops.

## Slide 10
Any questions?