## Slide 1: PowerPoint 2: Substructure
PowerPoint sentation
7. Building technology principles
7.2 Forms of construction

## Slide 2: Substructure
All buildings start with the substructure. This is all the structure below ground, up to and including the damp proof course (DPC).
The purpose of the substructure is to receive the loads from the superstructure and transfer them safely down to a suitable load-bearing layer of ground.
Elements of the substructure:
foundations
basements
retaining walls.

## Slide 3: Foundations
The foundations are the main element of a substructure. They ensure that all dead and imposed loads are safely transmitted through to the subsoils on which the building is constructed. Failure to adequately transmit the loads and select a suitable type of foundation will result in the stability of the building being compromised and, potentially, structural damage.

## Slide 4: Basements
A basement is a part of a building, either partially or completely below ground. Basements are not often incorporated into new developments, but are more popular in areas where there is a high demand for living and the cost of land is high. In areas such as London, residents are converting and creating basements to provide extra liveable space. Legislative constraints are a big consideration.
Advantages | Disadvantages
Floor area | Waterproofing
Space | Drainage
Privacy | Ventilation
Sloping sites | Natural light

## Slide 5: Retaining walls
Retaining walls are vertical structures designed to retain a material on one side – most commonly soil.
Retaining walls can be incorporated into a building’s design or be part of a landscaping design.

## Slide 6: Site investigations
In the early stages of the design process, site investigations should be carried out to gather information on the proposed site. The data that will need to be collected includes:
position of boundary fences and hedges
location of underground services including gas, water, electricity and drains
existing buildings that need to be demolished or protected
position, height, girth and spread of any trees on the site boundary
types and properties of the soil.

## Slide 7: Soil investigations
Subsoils can be many different types and have different load-bearing capacities. Soil investigations must be carried out to identify the type and properties of the soil so an appropriate type of foundation can be selected.
Soil type | Bearing capacity
Rock | High
Granite | High
Loose sand | Low
Peat | Low
Chalk | High
Compact sand | High
Silt | Low
Soft clay | Low

## Slide 8: Site clearance
This is the process of removing existing buildings, waste, vegetation and topsoil. It is not suitable to build on topsoil as the surface layer is difficult to compact down and it contains various chemicals that promote plant growth.
The process of removing topsoil can be costly and requires prior consideration in terms of transportation and labour. During the site investigations the site engineer will determine the volume of soil that requires removal. Some sites may have storage areas or garden plots available. If this is not the case then storage and transportation must be planned.

## Slide 9: Foundations in detail: trench excavation
In modern construction, trenches will generally be excavated using mechanical aids rather than manual labour. Using machines results in higher costs due to the equipment required but reduces the amount of labour and time spent on the excavation work.
For small building extensions or where accessibility is poor, manual excavation may be the most appropriate method.

## Slide 10: Trench support
Trench support prevents trenches from collapsing in on themselves. The types and extent of the support will depend on the depth of the trench and the subsoil stability. In modern construction it is common for steel rails and sheeting to be used rather than traditional materials such as timber.
A mixture of materials may be appropriate depending on the characteristics of the soil. Site engineers will make calculations to identify the appropriate support requirements for trenches.

## Slide 11: Selecting the right foundations
Consider:
the ground conditions
the soil type
any loads that may be generated either by the structure or naturally
the location of drains and trees in relation to the proposed building.

## Slide 12: Strip foundations
Strip foundations are a common choice of foundation for use in low-rise residential construction up to three storeys.
The concrete strip spreads the load of the heavy walls. The width of the strip depends on the load of the building and the bearing capacity of the soil.
There are two main types of strip foundation:
narrow strip
wide strip.

## Slide 13: Narrow and wide strip foundations
Narrow strip
Wide strip

## Slide 14: Raft foundations
These are commonly used on soils with poor bearing capacity or where subsidence is likely to occur. Raft foundations can withstand small settlements in the soil and act by spreading the load over the entire area of the ground floor of a building.

## Slide 15: Pad foundations
These are commonly used on large purpose-built structures such as industrial units or commercial buildings to support large, roofed structures. Pad foundations are rectangular or circular pads used to support localised loads such as columns.

## Slide 16: Other foundation types
Pile foundations are typically used for large structures and where poor soil will not prevent excess settlement. They transfer the load of a building to a much deeper subsoil that has a higher bearing capacity.
Driven piles can be driven into the ground using either a vibration driver or a pile driver. This method can be disruptive to surrounding areas and residents as it involves hammering the pile into the ground.
Bored piles: a cylindrical hole is bored using a large auger and is then filled with concrete. Often these piles are reinforced with a metal cage before pouring the concrete.

## Slide 17: Pile foundations

## Slide 18: Foundation reinforcement
Concrete is a prime element used in the formation of foundations. As a material, concrete has a high compressive strength but is weak in tension. Steel reinforcement can be incorporated into the foundation design to provide extra strength and avoid cracks occurring in the foundations.

## Slide 19
Any questions?