## Slide 1: PowerPoint 5: Building regulations and approved documents
PowerPoint
7. Building technology principles
7.3 Key content and required notifications of UK building regulations and approved documents

## Slide 2: History of building regulations
In the UK, formal building regulations have been in existence since the Great Fire of London of 1666 caused two thirds of the city’s structures to burn to the ground. After such destruction, measures had to be taken to prevent similar catastrophic evens occurring again.

## Slide 3: Modern building regulations
Building regulations set minimum standards and expectations for both the design and construction of buildings. The purpose of the regulations is to ensure the safety of the building as well as the health and safety of the people who occupy or use it.
Building regulations often change with new technology and government policies. You must check you have the most up to date copies of the approved documents.

## Slide 4: Building control: building regulation approval
Building regulation approval is different from planning permission and you might need both for your project.
You can apply to any local authority building control department or approved inspector for building regulation approval.

## Slide 5: The purpose of building control
Ensure standards.
Safety and hygiene.
Improve energy efficiency.
Reduce water wastage.

## Slide 6: Legislation
The Building Act 1984 and the Sustainable and Secure Buildings Act 2004 are the Acts of Parliament that produced the building regulations and approved documents. These acts are enforced by law and give power to building control officers.

## Slide 7: Legal obligations
The Building Act 1984 was passed by Parliament and is therefore a legal and enforceable Act.
The Building Act gives local authorities, via building control officers, the power to inspect and action any work which does not meet the provisions in the approved documents.
Builders and contractors have a legal obligation to comply when undertaking any construction work that qualifies for building regulation control.

## Slide 8: Building regulations

## Slide 9: Building regulations: enforcement
Building regulations are enforced through:
the checking of construction documentation including plans and specifications that are submitted to the local authority
the inspection of building works by a building control officer onsite.

## Slide 10: Approved documents
Building regulations only state the outcome of a construction activity. The regulations do not instruct how building works are carried out.
To help builders meet the building regulations there are approved documents specifying how work should be carried out.

## Slide 11: Approved documents
Part A – Structure
Requires all buildings to be designed, constructed or altered to be structurally safe and not impair the structural stability of surrounding buildings.
Part B – Fire safety
Covers all measures to provide safety from fires for residents, people in the vicinity of the building and firefighters. Guidance covers means of escape, fire detection and warning systems.

## Slide 12: Approved documents
Part C – Site preparation and resistance to contaminants and moisture
Covers weather and water tightness of buildings, subsoil drainage, site preparation, contaminated land and other related hazardous and dangerous substances.
Part D – Toxic substances
This controls hazards from the toxic chemicals used in cavity insulation systems.

## Slide 13: Approved documents
Part E – Resistance to the passage of sound
Requirements for sound insulation between buildings, including new dwellings and conversions of existing buildings to form dwellings. Covers sound reduction between rooms and acoustic conditions for common areas in flats and schools.
Part F – Ventilation
Covers standards for ventilation and air quality for all buildings. Condensation is also covered.

## Slide 14: Approved documents
Part G – Sanitation, hot water safety and water efficiency
Sets out standards for provision of sanitary and washing facilities. Also covers bathrooms and hot water systems and safety requirements for unvented hot water systems.
Part H – Drainage and waste disposal
Provides guidance on adequate drainage and pollution prevention. Technical design standards cover sanitary pipework, foul drainage, rainwater drainage and disposal, wastewater treatment, discharges and cesspools.
There is no Part I in the documents …

## Slide 15: Approved documents
Part J – Combustion appliances and fuel storage systems
Covers the construction and installation of boilers, chimneys, flues, hearths and fuel storage installation. This section also covers requirements to control fire sources and prevent burning, pollution and carbon monoxide poisoning.
Part K – Protection from falling, collision and impact
Sets standards for the safety of stairways, ramps and ladders. Also includes guarding against and warnings about hazards.

## Slide 16: Approved documents
Part L – Conservation of fuel and power
Controls the insulation values of building elements. Also covers mechanical ventilation, air conditioning systems and carbon index ratings.
Part M – Access to and use of buildings
Covers the inclusive provision of ease of access to and circulation in all buildings along with requirements for facilities for disabled people.

## Slide 17: Approved documents
Part N – Glazing safety
Withdrawn in 2013, now covered by Part K.
No Part O …
Part P – Electrical safety
Covers the design, installation, inspection and testing of electrical installations in order to prevent injuries from electrical shocks and burns and prevent injuries arising from fires due to electrical components overheating.

## Slide 18: Approved documents
Part Q – Security
Sets out that provision must be made to resist unauthorised access to any dwelling and any part of a building from which access can be gained to a residence within that building.
Part R – Physical infrastructure for high speed electronic communications networks
Introduces a new requirement for in-building physical infrastructure which enables connections to broadband networks.
Regulation 7, ‘Materials and workmanship’ is also part of this list and covers the use of appropriate materials for a building and how people working on the building must behave.

## Slide 19: Role of the building control officer or inspector
    Checking of plans for approval.
    Giving advice on construction.
    Maintaining an approved standard.
    Inspections.
    Dealing with dangerous structures.
    Demolition notices.
    Enforcement work.

## Slide 20: Building notice
A building notice is a form that must be completed when building works are about to begin. It informs building control where the work will take place and when.

## Slide 21: Building inspection
A building inspector will need to inspect works at certain stages of a project.
Commencement
Foundation excavation
Foundation constructed
Ground floor oversite
Damp proof course (DPC)
Steel beams/structural alterations
Drains (before backfilling)
Drains (testing)
Completion

## Slide 22: Prosecution and non-compliance
It is important to notify building control/inspection at each key stage, as failure to do so can result in prosecution and an unlimited fine may be imposed.
The council can also have any non-compliant building work removed or rectified.

## Slide 23: Unauthorised building work
It is an offence to carry out notifiable building work without submitting full plans or building notice application.
Carrying out unauthorised work can lead to prosecution and will almost certainly create difficulties when a property is sold. Building regulations make provision for a regularisation application.

## Slide 24: Enforcement procedures
If work does not meet the requirements of the approved documents a building inspector has the authority to remove or have altered any such work. This involves serving a 28-day notice on the owner. If the work is not completed to the correct standards, then the local authority may do the work and later recover the costs.
An authorised building control officer has the right to enter premises to find out whether or not there is a contravention of the building regulations. A local authority has the right to obtain a warrant if entry is refused. Legal action could result from failure to gain entry because of obstruction.

## Slide 25
Any questions?