## Slide 1: PowerPoint 8: Building and structure and fabric
PowerPoint presetation
7. Building technology principles
7.7 Building structure and fabric
7.8 Approved Documents and guidance for penetrating building structure and fabric

## Slide 2: Building fabric or envelope
As you learned from Session 4, the external fabric of a building (also known as the envelope) consists of the materials and components that form the shell of the building. This includes walls, floors, roofs, windows and doors. These may be load-bearing or non-load bearing depending on design and structural form.

## Slide 3: Building fabric
The fabric of a building:
protects occupants from the elements
regulates the internal environment in terms of temperature, humidity and moisture
provides privacy and security for occupants
provides access from the interior to the exterior of the building.

## Slide 4: Building materials
There are many different building materials that can be used to create the structure of a building. The materials used will depend on the design and context of the project. There are certain aspects to consider when selecting the correct materials for different elements of a building. These factors can include:
building regulation requirements
the structural properties of the material
location of use: internal/external environmental factors
cost implications.

## Slide 5
Timber
Timber is a traditional building material that is readily available and versatile. Once treated, timber can be used externally and is classified as a sustainable material. Timber can be used for many different aspects of a building.
Advantages
Disadvantages
Susceptible to rot
Fire protection
Adaptability
Natural defects
Tensile strength
Aesthetic appeal

## Slide 6: Concrete
High compressive strength
Low tensile strength
Fire protection
Durability
Low strength to weight ratio
Concrete is a frequently used building material for construction and civil engineering purposes. One of the main benefits of concrete is its compressive strength and durability. In commercial and industrial contexts concrete is often used to create the structural frame of a building. Concrete can be pre-cast or formed in situ to the desired shape and size depending on the design specification.
Advantages
Disadvantages
Susceptible to cracking
Adaptability

## Slide 7: Steel
Steel is one of the most commonly used structural building materials. Steel portal frame systems are widely used in commercial and industrial contexts. Steel can often be used in conjunction with other building materials such as concrete to provide extra strength and reinforcement.
Relatively low cost
Versatile
Reliability
Erection time
High maintenance costs
Fire-proofing costs
High strength to weight ratio
Advantages
Disadvantages
Inflation costs

## Slide 8: Masonry
Masonry is a traditional construction material. In modern construction, masonry is still widely used and a key aesthetic feature in our British architecture. Cavity walling is a modern form of masonry. Traditionally used for domestic dwellings, it is now a common method in commercial and industrial contexts. Masonry is very strong in compression but less effective with lateral loading.
Bricks (engineering bricks, facing bricks, etc).
Blocks (solid concrete, hollow concrete, etc).
Mortar (cement, additives, water, lime, etc).
Materials

## Slide 9: Cladding

## Slide 10: Fenestration
The term ‘fenestration’ refers to the openings in a building’s fabric in relation to the quality, quantity and characteristics of the building aesthetics. Openings include windows, doors and skylights.

## Slide 11: Supports and fixings
Supports and fixings should be selected in accordance with building regulations and manufacturers’ instructions. An understanding of the building’s fabric and materials should be formed to select appropriate types of fixtures and fittings. Different building materials will require different supports and fixings, taking into account load rating of fixings and environmental factors.
Example
In high-moisture areas, stainless steel fixings would be suitable as they are less likely to corrode.

## Slide 12: Hazards
Failure to select the correct supports and fixings for the building fabric can often lead to equipment not been securely fixed, increasing the risk of hazards associated with falling objects.
Selection and use of unsuitable fixtures and fittings may also reduce the lifespan of equipment and lead to increased maintenance costs.
Manufacturers’ instructions can be used to identify suitable usage and provide extensive information on the installation, maintenance and operational use of a product.

## Slide 13: Approved documents and guidance for penetrating building structure and fabric
Penetrating the structure and fabric of a building to install electricity, gas, water, drainage or other systems, if done incorrectly, could impair the building’s structural integrity and performance, causing failures.
It could also cause other defects, such as impeding the building’s ability to be fire and weather resistant, allowing moisture into the building’s structure, allowing unwanted noise to travel through the building, or reducing its insulation levels and increasing its carbon footprint.
Approved documents give guidance on penetrating the building structure and fabric to minimise any effects on its performance.

## Slide 14: Part A: Structure
Requires all buildings to be designed, constructed or altered to be structurally stable and safe. It includes diagrams of the structural elements of a building and stipulates design standards. This also includes guidance on not impairing the structural stability of surrounding buildings.
Approved Document A | Part A - Structure | Planning Portal

## Slide 15: Part B: Fire safety
Covers all measures to provide safety from fires for building residents, people in the vicinity of the building and firefighters. Guidance covers means of escape, fire detection and warning systems. There are two volumes of approved document B: Volume 1 for domestic dwellings and Volume 2 for other building contexts.
Approved Document B - Volume 1: Dwellings | Part B - Fire Safety | Planning Portal
Approved Document B - Volume 2: Buildings other than dwellings | Part B - Fire Safety | Planning Portal

## Slide 16: Part B: Fire safety
Examples of measures to increase fire safety include:
pipes penetrating the structure: make the opening in the structure as small as possible and provide fire-stopping between pipe and structure
ensure the material of penetrating flue walls is fire resistant to at least the level of half the wall.

## Slide 17: Part C: Site preparation and resistance to contaminants and moisture
Covers weather and water-tightness of buildings., subsoil drainage, site preparation and contaminated land as well as all other related hazardous and dangerous substances.
Approved Document C | Part C - Site preparation and resistance to contaminants and moisture | Planning Portal
For example, penetrations for pipes or services should be filled and sealed to reduce condensation and ingress of water.

## Slide 18: Part E: Resistance to the passage of sound
These requirements cover sound insulation between buildings, including new dwellings and conversion of existing buildings to form dwellings. Sound reduction between rooms and acoustic conditions for common areas in flats and schools are also covered.
Approved Document E | Part E - Resistance to the passage of sound | Planning Portal
For example, see Diagram 3.6, page 46, ‘Floor penetrations’. The diagram shows what insulation is required to minimise noise travelling through holes made to accommodate pipework. What other examples can you find?

## Slide 19
Any questions?