## Slide 1: PowerPoint 10: Drawings, circuit diagrams and schematics
PowerPoint n
8. Construction information and data principles
8.4 Drawings, circuit diagrams and schematics

## Slide 2
Paper sizes
PowerPoint presentation
You will already be familiar with some of the international standard paper sizes (eg A3, A4 etc).
Drawings

## Slide 3: Drawings
Scale
Scale is the size that a drawing has been produced to. Actual size is 1:1. Where the scale is 1:100, it means that the actual size is 100 times greater than that shown on the drawing.
If responsibility for determining dimensions are with another party, the scale may be followed by the statement ‘do not scale’ or ‘not to scale’ on the drawing.

## Slide 4
PowerPoint presentation
Border:
To ensure whole drawing is included in reproductions
Typical sheet layout
Title block:
Usually in the bottom right-hand corner
Drawn by:
Technician’s name
Checked by:
Lead designer’s name
Approved by:
eg head of department
Date:
Drawing completed
Drawing no.
Usually a project reference followed by a sheet no. eg KWL/14
Drawing title:
Name of drawing (dwg)
Project title:
Paper size:
eg A3
Scale:
eg 1:100 when printed at paper size shown
Rev.:
Drawing revision, documented following changes to the drawing
Business LOGO &
address
SH
RBE
HD
1/02/21
Central Point Development
SWANSEA
KWL/14A
A3
A
1:100
Location Plan

## Slide 5: Site plans
A site plan is a large scale drawing that shows the whole site for an existing or proposed development. Site plans are usually at 1:500 or 1:200. For a small project, larger scales may be used. The information shown on a site plan will vary depending on the size and type of project, however the following information is likely to appear on most site plans.
Notes highlighting changes from previous revisions.
North arrow.
Key dimensions.
Materials.
Site boundaries and delineation of adjacent properties.
Trees, tree protection orders and the main elements of the landscape.
Parking areas with dimensions or capacities, traffic flows and signage.
Roads, footpaths, ramps, paved areas and easements (rights of ways etc.).

## Slide 6: Site plan

## Slide 7
PowerPoint presentation
Detailed design drawings
A detailed design drawing shows the intended locations of plant items and service routes in such detail as to indicate the design intent. The main features of detailed design drawings should be plan layouts to a scale of at least 1:100, plan areas to a scale of at least 1:50, accompanied by cross-sections.
To view examples of detailed design drawings, go to:
https://www.indiefolio.com/project/579871df7e290/detail-drawings

## Slide 8: Installation drawings
Installation drawings are used by the operative to install building services to the design created by the mechanical or electrical design engineer. Operatives follow these drawings to establish location, route and size of services throughout the project. This drawing may change throughout the project and new versions, called ‘revised drawings’ may be issued.
Installation drawings are developed from detailed drawings. Installation drawings define the information needed by onsite operatives to install the system or system component.
Notes: For more information on what is included in an installation drawing, go to: Installation drawings - Designing Buildings Wiki

## Slide 9: ‘As fitted’ drawings
An ‘as fitted’ drawing shows the completed project once the services have been installed and the project has been handed over to the client.
These drawings are a reference for the client and any contractor who may carry out repairs or maintenance at a later date, and should contain instructions for how to maintain or deconstruct the works as necessary.

## Slide 10: Schematics
A schematic diagram (often simply called a schematic) can serve many purposes but is primarily provided to show the overall functionality of a system.
It includes every component that a system contains, with each component having its own special symbol. A schematic is a line diagram that describes the interconnection of components in a system in a two-dimensional layout, with divisions that show distribution between building levels.
It may also be an isometric-style diagram showing the distribution of systems across individual floor levels.

## Slide 11: Schematics (cont.)
Schematics show the relationship between components within a system. For examples, a heating schematic may show major components around a boiler installation, instructing the installer on where components should be installed in relation to each other.
All the functional components that make up the system are shown using symbols and line conventions in accordance with industry standard guidance.
Schematic drawings tend to use a small scale to allow close detail to be shown.
Notes: For more information see: Schematic - Designing Buildings Wiki

## Slide 12: A typical schematic drawing
Notes: Schematic diagram reproduced with kind permission of BSRIA.

## Slide 13: Wiring diagram
A wiring diagram is a simple visual representation of the physical connections and physical layout of an electrical system or circuit. It shows how the electrical wires are interconnected and can also show where fixtures and components may be connected to the system.
Wiring diagrams show how the wires are connected and where they should be located, as well as physical connections between all the components.
Notes: Wiring Diagram (smartdraw.com)

## Slide 14: Sample wiring diagram

## Slide 15: Circuit diagram
A circuit diagram is a visual display of an electrical circuit using either basic images of parts (pictorial diagram), or industry standard symbols (schematic diagram). The symbols used depend on the audience for the diagram.
A schematic circuit diagram is used to give a visual representation of an electrical circuit to an electrician. A pictorial diagram is aimed at a broader, less technical audience.

## Slide 16: Sample circuit diagram

## Slide 17: Line diagram
A line diagram shows the location of the main items of plant, routes of main pipes, air ducts and cable runs in detail, to illustrate the incorporation of engineering services within the project as a whole.
A single-line diagram is also sometimes called a one-line diagram and is a simplified form of notation for representing a three-phase power system (used mostly in power flow studies).

## Slide 18: Single line diagram of 11kV substation

## Slide 19: The graphic symbols used for electrical components in circuit diagrams are covered by national and international standards, in particular IEC60617 (also known as British Standard BS3939). The Institution of Engineering and Technology (IET) Wiring Regulations is currently in its 18th edition (BS7671:2018), published in July 2018. It came into effect in January 2019. From this date, all new and amended electrical installations must conform to its requirements.
BS 7671
For more information see: BS 7671 - 18th Edition - IET Wiring Regulations (theiet.org)
Notes: For more information see: https://www.theiet.org

## Slide 20: Standards for units and symbols
Standard | Content
BS 4058:1987 | Data processing flowchart symbols, rules and conventions
BS 5070:1990 | Engineering diagram drawing practice. Part 4 recommendations for logic diagrams
BS EN ISO 80000-1:2013 | Quantities and units – general
BS EN 80000-6:2008 | Quantities and units – electromagnetism
BS EN 60027-1:2006 | Letter symbols to be used in electrical technology – general

## Slide 21: Symbols ‒ electrical connections and network elements
PowerPoint presentation

## Slide 22: Symbols ‒ logic and optic fibre

## Slide 23: Symbols ‒ telecommunications
PowerPoint presentation

## Slide 24: Common electrical abbreviations
Per unit: pu
Root mean square: rms
Alternating current: AC
Direct current DC
Electromotive force: emf
Phase: ph
Potential difference: pd
Power factor: pf

## Slide 25: Symbols ‒ plumbing
PowerPoint presentation

## Slide 26: Symbols ‒ plumbing
PowerPoint presentation

## Slide 27
Any questions?