## Slide 1: PowerPoint 2: Data sources
PowerPoint sentation
8. Construction information and data principles
8.1 Data

## Slide 2: Data sources
There are a variety of data sources which are used in construction and building services engineering.
Data from these sources can be used to understand behaviour, assess performance, improve market competitiveness, allocate resources and manage costs. In this presentation we look at:
  operational cost monitoring
  enterprise systems
  utilities, building services, meters, building management systems
  infrastructure and transport.

## Slide 3: Operational cost monitoring
Operational costs are those incurred by the day-to-day operation of a building, sometimes referred to as running costs. They include:
wages
utilities
maintenance and repairs
rent
sales
general and administrative expenses.
In broad terms, operational costs begin once a client takes possession of a completed development. A higher quality asset (building) may have lower maintenance, utility and repair costs.

## Slide 4: Additional operational costs
Provision of amenities such as a bar, canteen or gym.
The costs of adapting a building to meet changing user requirements.
Sometimes the layout and design of a building dominates the way certain operations are carried out, the number and type of staff employed and hence the overall operational costs.
The prospective building owner must be made aware of the effects a design might have on operational costs. For example, the choice of temperature control in offices can affect the efficiency of employees.

## Slide 5: Estimating expenditure tool
The Royal Institution of Chartered Surveyors (RICS) has online tools to help facility managers and surveyors work out maintenance and operating costs. These are usually offered at a yearly subscription, and can assist in:
producing life cycle costings
benchmarking, planning and budgeting
forecasting, estimating and cost control
calculating running and refurbishment costs
comparing component costs and how they will last over time, thus informing decisions made at the beginning of a project.
https://www.rics.org/uk/products/data-products/facilities-management/building-running-costs-online/

## Slide 6: Estimating expenditure tool
Examples of data that can be provided by the tool include:
administration costs (building maintenance, decoration, fabric, operations, cleaning, utilities)
figures for the life expectancy of over 300 common building components including substructure, superstructure, finishes, fittings, furnishings and external works
comparisons of the running costs of different building types over different timescales
information on deterioration or failure of components
a selection of the most common wage agreements and dayworks rates
average costs of refurbishment by building type.

## Slide 7: Enterprise systems
Enterprise systems are software packages that support business processes, such as:
data analytics
information flows
reporting.
They can integrate a number of different applications and replace independent systems that may or may not interact, and process data to support particular business functions. They are generally called packaged enterprise application software (PEAS) but can also be custom made. Types include:
enterprise resources planning (ERP) systems,
enterprise planning systems
customer relationship management software.

## Slide 8: Enterprise systems
  PEAS performs the following functions via a computer network:
order processing
procurement/purchasing systems
production/work scheduling
customer information management (CIM)
energy management
performance reporting
accounting.

## Slide 9: Enterprise resource planning
    accounting
    budgeting and forecasting
    CRM
    human resources
    inventory management
    supply chain management.
    This data is collected from various departments across a business. ERP is an integrated system which operates in real time and has a common database supporting all applications. It can be cloud-based or onsite.
  Enterprise resource planning (ERP) is a type of enterprise system that tracks resources such as:

## Slide 10: ERP
ADVANTAGES | DISADVANTAGES
Can speed up workflows. Can sort data by profit centre, location, etc, to assist informed decision making. A common control system manages the security permissions across the business. The ability to monitor day-to-day processes provides a mechanism for continuous improvement. A single system facilitates a standard single naming system. | Implementation can take up to two to three years. Can be costly, depending on scale. May require hardware to be updated. Every user will need training on the ERP system. It can take time to migrate existing data into the system. Can be too complicated for large-scale companies.

## Slide 11: Public utilities and building services
Utilities are services provided directly by companies, which are generally the only source for those services, such as electricity, gas, water, telephone, internet, etc.
Following deregulation, the ‘public’ utility services are often privately owned, but the term separates them from ‘private’ utility services. Public utility providers determine how each product will be provided, the apparatus and equipment used to supply it and the demarcation point –the ownership boundary.
Building services are any services provided by the building, and not from an outside provider. Building services engineers need to coordinate the requirements of the utility provider with the particulars of the building. This includes the provision of space, rooms and distribution routes, together with any specific access requirements, finishes and building services systems.

## Slide 12: Private utilities
Private utility services are those produced by a building for its own use, such as local diesel generators, solar power, wind turbines and boreholes for water.
Utility services may be buried in the ground, fixed to buildings and other structures, suspended in the air or distributed wirelessly.

## Slide 13: Information from building services engineers
Building services engineers are responsible for determining the availability, quality, reliability, capacity and supply conditions of utility services required from the public utility services provider to meet the needs of the building.
The process of obtaining planning permission is usually led by architects with input from building services engineers in the following areas, for which they will need to have accurate data:
the orientation of the building and elevations, size and locations
louvres and windows with respect to heating and cooling loads and the availability of daylight
location of any external, visible building services equipment.

## Slide 14: Information from building services engineers
Building services engineers are also responsible for the following information.
Developing a utilities statement describing how a building will connect to existing utility infrastructure systems. This includes how the design incorporates any utility company requirements for substations etc. and confirmation that service routes have been planned to avoid the potential for damage to trees or wildlife.
Foul and surface drainage requirement information – connection to sewerage and soakaways.
Developing a ventilation/extraction statement for buildings such as restaurants, or where fumes have to be extracted. This includes plans showing the location of equipment and external vents and detailed drawings of the design of the equipment, pipework and flues.
Information about artificial lighting – layout plans showing the location of all light fixtures, beam orientation, spread patterns and specified lux levels.

## Slide 15: Metering
In order to address the Part L requirements of the building regulations, and monitor energy consumption, a specification of metering may be required for new builds and/or major refurbishments.
A good metering strategy is an essential energy management tool. However, it is the action that results from the analysis and interpretation of the data that saves energy.
The following are key objectives for metering:
ensure system efficiency
collect data for reporting, regulatory compliance and baselining
inform design and investment decisions
inform infrastructure management
provide visibility/usability of energy data.

## Slide 16: Metering
CIBSE TM39 provides a methodology for submetering and this is linked to CIBSE TM31 on building energy log books.
Both of these documents provide good practice energy advice and are Part L ‘second tier’ referral documents that promote best practice in the design of energy metering and submetering (not smart metering) in non-domestic buildings.

## Slide 17: Building management system (BMS)
heating, ventilation and air conditioning (HVAC)
lighting
energy
fire and security systems (smoke detection, alarms, CCTV etc)
ICT systems
lifts
smart meters.
A building management system (BMS), sometimes called a building automation system (BAS), is a computer-based system (software and hardware), installed to control and monitor a wide range of building services:

## Slide 18: BMS
BMSs show how buildings are operating in real time and allow building managers to control and adjust the system for optimum performance.
A BMS can provide:
visualisation of the data with a graphic user interface (GUI)
reports on building performance
time scheduling of building operations
alarms and alerts for faults and failures
comparisons between buildings and benchmark data.

## Slide 19: Control systems
Control systems are an essential part of buildings and the management of the internal environment. When buildings do not satisfactorily meet the occupants’ requirements, this is often due to problems with the controls. Control irregularities are also a significant cause of excessive energy consumption due to:
an inappropriate controls concept,
poor design and/or poor equipment selection (eg low quality sensors)
incorrect commissioning
inadequate maintenance.
While maintenance may not be responsible for a particular fault in a control system, it can identify and rectify problems originating from earlier work, including improvements to the control system design.
Building management systems may now be integrated with building information models (BIM) to allow performance in use to be compared with design criteria and design simulations. This can help identify potential problems in operation or design and can help validate modelling techniques. Building information models might also include information about the operation and maintenance of building components.

## Slide 20: Building energy management system (BEM)
A building energy management (BEM) system control energy-related systems such as HVAC, lighting and power systems.
When programmed skilfully, a BMS can become a BEM. To do this, the BMS needs to have a programmed control strategy that takes into consideration all the aspects of the plant connected to it and the synergy between them.

## Slide 21: Infrastructure and transport
In the UK, there are 13 critical national infrastructure sectors: chemicals, civil nuclear, communications, defence, emergency services, energy, finance, food, government, health, space, transport and water. The loss or compromise of these critical services would cause a major impact. Infrastructure data sources include:
the Critical National Infrastructure (CNI) knowledge database which holds data about the UK’s critical infrastructure
the National Infrastructure and Construction Procurement Pipeline, which provides detail on investment in UK infrastructure
the Office for National Statistics
the gov.uk website (Infrastructure and Projects Authority – IPA).

## Slide 22: Infrastructure and transport
A variety of data and reports are available from the gov.uk website which are relevant to construction industries, such as:
electric vehicle charging infrastructure statistics
infrastructure, assets and emissions
major projects data
communications infrastructure
distributed energy infrastructure
national infrastructure planning
annual reports
project delivery framework.
https://www.gov.uk/government/organisations/infrastructure-and-projects-authority

## Slide 23
Any questions?