## Slide 1: PowerPoint 12: Access equipment and manual handling of loads
PowerPoint presentation
1. Health and safety in construction
1.13 Safe practices and procedures for the use of access equipment and manual handling

## Slide 2: Objectives
At the end of the session learners should be able to:
  identify the different types of access equipment and the safety checks required
  demonstrate safe erection methods of access equipment
  understand and demonstrate safe manual handling techniques.

## Slide 3: Access equipment
Access equipment comes in many different forms, depending on the job to be completed. For example:
  ladders (roof, step etc)
  mobile access towers
  trestles, platforms and podiums
  staging and booms
  scissor lifts.

## Slide 4: Access equipment
Access equipment allows you to work at different heights for short periods of time. Before using such equipment you should take time to ask yourself about:
  Use?
  Duration of work?
  Type required (eg what type of ladder do I need)?
  Loads to be carried?
  Prevention of and consequences of falls?
  Wear and tear of the equipment?
  Frequency of access?
  Is the access equipment fit for purpose?

## Slide 5: Operative competency
All operatives should be trained on how to use each piece of access equipment correctly and safely. Remember, all access equipment must be checked prior to each use to ensure safety.
Ladders – ensure that the ladder is on firm and level ground, tied off, set at the correct angle and of the correct class.
Platforms – ensure they are on firm and level ground and assembled as per manufacturer’s instructions.
Scaffolds and mobile scaffolds – ensure they are on firm and level ground and assembled as per manufacturer’s instructions.
Mobile elevated work platforms – used as per training and within set limits.

## Slide 6: Tagging
All access equipment such as ladders and scaffolds will need to be checked regularly to ensure it is fit for purpose.
All platforms, mobile scaffolds and scaffolds use a tagging system to state when they were last checked and if they are safe to use.
However, all access equipment should be checked prior to each use to ensure safety.

## Slide 7: Ladders
Ladders come in many forms, for example:
  single, double and triple extension ladders
  roof ladders
  step ladders.
These will be considerd further at over the next few slides.

## Slide 8: Single ladders
    These ladders do not extend and are of a
    single length.
    They can be manufactured from wood,
    aluminium or fiberglass.

## Slide 9: Triple ladders
    These are primarily 3 ladders that
    can extend to even greater heights.
    They can also be manufactured from
    wood, aluminium or fiberglass.

## Slide 10: Ladder classes
The previous types of ladder are available in three classes.
  Class 1 – industrial – heavy-duty with a load capacity of not more than 175kg.
  Class EN131 – commercial – medium-duty with a load capacity of not more than 150kg (suited for painting or similar tasks).
  Class III – domestic – light-duty with a load capacity of not more than 125kg.

## Slide 11: Roof ladders
    These ladders are used to climb up
    onto a roof.
    They can be manufactured from
    wood, aluminium or fiberglass.

## Slide 12: Step ladders
    These ladders are used when you only require a
    small amount of elevation.
    They can be manufactured from
    wood, aluminium or fiberglass.

## Slide 13: Ladder checklist
The following checklist should be completed for all ladders prior to use.
  Any damage or missing parts?
  Any loose bolts or joints?
  Any faulty welds or cracks?
  Are hooks and locks in good condition?
  Are the grips on the rungs free from mud or grease to prevent slips?

## Slide 14: Erecting a ladder
When erecting a ladder, the following guidance should be followed.
  The ladder should be erected on firm and level ground.
  The angle of the ladder should be 75 degrees (the ‘1 out for 4 up’ rule).
  Extend above the landing point by 1.07m (or 5 rungs).
  Ensure there are no hazards above, below or near where you are going to erect the ladder.

## Slide 15: Mobile access towers
    Also known as ‘MATs’, these are usually specially designed
    made from light aluminium alloy tube.
    The tower is built by slotting the sections
    together as per the manufacturer’s
    instructions until the desired height is
    reached. It is imperative to follow the
    manufacturer’s guidance to ensure the
    tower is assembled safely and correctly.

## Slide 16: Trestles, platforms and podiums
    These types of access equipment are
    designed to provide access to working
    at height for longer durations and at
    lower levels.
    This is a work trestle.
    These platforms should be positioned
    on a firm and level surface to ensure
    safety.
                Source: 3947.jpg (400×400) (sealantsandtoolsdirect.co.uk)
Use of images is great.
Copy in the image.
Note details of the image and its source on the artwork log.

## Slide 17: Trestles, platforms and podiums
    This is a work platform.

## Slide 18: Trestles, platforms and podiums
    This is a low work podium.

## Slide 19: Staging
    This type of access equipment can be
    bolted to two sets of ladders to create
    a work platform at various heights.
    It is imperative to assemble this
    specialist piece of equipment correctly.
    This is an example of staging.

## Slide 20: Boom
    A boom is a method of working at
    height using a mechanical lift
    that is controlled by the operative in the
    cradle.
    This mechanical elevated work platform
    can be moved around using its motor
    and is sometimes called a ‘cherry picker’.

## Slide 21: Scissor lift
    A scissor lift is another method of
    working at height using a mechanical
    lift that is controlled by the operative in
    the cradle.
    This mechanical elevated work platform
    can be moved around using its motor.

## Slide 22: Manual and mechanical handling
Incorrect manual handling causes many injuries when working on a construction site, and back strains and associated injuries are the main cause of time off work.
The Manual Handling Operations Regulations (MHOR) 1992 is the piece of legislation governing manual handling.
Careful planning means using risk assessments to ensure that no harm is caused to you or others during a lifting procedure.

## Slide 23: Manual and mechanical handling
All activities that use mechanical lifting equipment are covered by the Lifting Operations and Lifting Equipment Regulations (LOLER) 1998.
If an item or object is too heavy or unstable, always use a mechanical lifting aid.
When manual handling, you can lift an object as a team with an identified leader. The team should be made up of people similar in height and strength.

## Slide 24: Manual handling: safe lifting weights

## Slide 25: Manual handling: lifting and carrying

## Slide 26: Mechanical lifting aids
Always risk assess before you lift.
Even if your supervisor asks you to carry a heavy object from a van, ask
for help or use a mechanical lifting aid.

## Slide 27: Small lifting equipment
There are many different types of small lifting equipment available to assist you.

## Slide 28
Any questions?