## Slide 1: PowerPoint 3: Codes of practice
PowerPoint presentation
1. Health and safety in construction
1.3 Approved construction codes of practice

## Slide 2: Objectives
By the end of the session, learners should be able to:
  state the reason for Approved Codes of Practice (ACOPs)
  understand where ACOPs sit in the hierarchy of the law
  identify various types of ACOP relating to the construction industry
  understand where to obtain relevant ACOPs.

## Slide 3: ACOPS
What is an Approved Code of Practice?
According to the Health and Safety Executive (HSE) website:
  … each ACOP is approved by the Health and Safety Executive, with the consent of the Secretary of State. It gives practical advice on how to comply with the law. If you follow the advice you will be doing enough to comply with the law in respect of those specific matters on which the Code gives advice. You may use alternative methods to those set out in the Code in order to comply with the law.

## Slide 4: ACOPS
‘So far as reasonably practicable’
The term ‘so far as reasonably practicable’ is used throughout health and safety law, but what does it mean?
It is a shortened way of saying that the cost in money or time to reduce a risk should be proportionate to the risk involved – ie if all options have been explored and it is technically impossible to eliminate the risk completely, reduce the risk further, or would cost a disproportionate amount of money to mitigate against the risk completely, then the risk should be managed as best as possible.
Guidance is provided by the HSE in the form of leaflets, books and web pages.
Legal status of HSE guidance and ACOPs

## Slide 5: Hierarchy of health and safety guidance
The overarching piece of health and safety legislation is the Health and Safety at Work Act (HASAWA) 1974, enforceable by law.
The next tier are the various regulations which have a specific focus on individual sectors or areas, eg Gas Safety Installation and Use Regulations 1998.
Then we have ACOPs, eg Approved Code of Practice L8: Legionnaires disease – The control of legionella bacteria in water systems.
Health and Safety at Work Act 1974
Approved Codes of Practice
Regulations

## Slide 6: Construction-related ACOPs
There are many construction-related ACOPs. Below are examples, coded as follows: health and safety guidance (HSG), industry guidance (INDG) and legal (L).
Asbestos: The Survey Guide, HSG264.
Gas Safety (Installation and Use) Regulations 1998; Approved Code of Practice and Guidance 5th edition, L56.
Working At Height: A Brief Guide, INDG401.
A Brief Guide to the Reporting of Injuries, Diseases and Dangerous Occurrences Regulations 2013 (RIDDOR), INDG453.
A Brief Guide To Working Safely, INDG258 (confined spaces).
Don't Lose Your Hearing, INDG363 Rev.2, INDG363.

## Slide 7: Where to obtain the latest ACOPs
Follow the link to the HSE website to find up-to-date health and safety, industry and legal guidance in the form of ACOPs.
HSE Books - the official Health and Safety Executive publications shop

## Slide 8
Any questions?