## Slide 1: PowerPoint 10: 4.7 Building Information Modelling (BIM)
4: Construction and the built environment industry

## Slide 2: BIM characteristics
Building Information Modelling is a method of planning and managing a construction project throughout the building’s lifecycle, from the design and planning stages through to demolition.
Its main characteristics are as follows.
  Extensive use of digitally processed information.
  Allows detailed analysis of design elements of a building, identifying potential problems before construction starts.
  Offers visualisation of structure and building layout using 3D digital modelling.

## Slide 3: Advantages and benefits of BIM
Building Information Modelling continues to develop as a method of working collaboratively on the design, construction and operation of buildings.
Some benefits are as follows.
  Complex design ideas can be presented in a medium that is easier for all personnel to work with.
  Team coordination and collaboration are supported at all stages of design and construction.
  Allows future operational aspects of a building to be considered to enhance efficiency and economy throughout the building’s lifecycle.

## Slide 4: BIM terminology
An extensive range of terminology has evolved to describe the features and functions of BIM.
Government promotion of the system has resulted in multiple levels of classification that apply the terminology to suit the designated BIM level.
The UK government’s 2011 Construction Strategy defined four levels of BIM to help clients and suppliers understand how BIM and digital technologies should be used on projects.

## Slide 5: BIM terminology (continued)
  Level 1. Projects will use a mixture of 2D and 3D CAD drafting. They will use a common data environment for the electronic sharing of data. This will often be managed by the main contractor and may be shared among team members.
  Level 2. Projects will use intelligent, data-rich objects in a managed 3D BIM environment. All parties working on a project are able to combine their BIM and design data to collaborate and share information through the use of a common data environment (CDE). The CDE enables users to carry out checks against data validation strategies to make sure they are on target.
  Level 3. Projects at this level are fully collaborative. They use a single, shared project view for data integration, which all parties can access and modify as allowed through process and security controls.
These are the level descriptions for Levels 1–3 from the government guidance documents.

## Slide 6: Common Data Environment (CDE)
In this session we will look at three examples of BIM terminology beginning with the Common Data Environment.
  The CDE is a single source of information for a project.
  It is used to collect, manage and distribute documentation digitally.
  It makes graphical and non-graphical data available for the whole team for ‘permitted purposes’.
  It allows collaboration and reduces duplication and mistakes.
An information manager may be appointed to ensure the data is kept secure.

## Slide 7: Digital Plan of Works (DPoW)
This is a central point of reference for specific information about:
  what is required
  when it is required
  who is expected to fulfil that requirement.
The DPoW gives a clear understanding of where contractors, sub-contractors and construction professionals ‘fit in’ to the work programme in collaboration with others.
This assists all members of the construction team to understand their obligations, supporting timely and effective decision making throughout the project.

## Slide 8: Employer’s Information Requirements (EIR)
The EIR sets out information required by the employer during the construction phase of a project.
  standardised methods for creating, naming and communicating information.
It can also extend into the handover and occupation phase to inform relevant employers managing the operation of the completed building.
It can include:
  role descriptions for those responsible for managing information.
The exact nature of the EIR will vary depending on the complexity and scale of the project.

## Slide 9: Using BIM
While mainly used for major projects, BIM can be applied to smaller projects to good effect.
As a system that uses shared information to create a digital representation of a building, BIM offers a reliable means for the construction team to make decisions on design, construction and operation of complex structures.

## Slide 10
Any questions?