## Slide 1: PowerPoint 16: Calculate maximum and minimum values using differentiation
PowerPoint presentation
4. Essential mathematics for engineering and manufacturing
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.

## Slide 2: Differentiation – stationary points
When a system is modelled by an equation, a stationary point occurs when the gradient is instantaneously equal to 0.
The graph shows the equation
There are two points on the graph where the gradient is 0.
A stationary point can either be a maximum or a minimum.
Notes: Tutor – ask students to point out these points and then draw horizontal gradients on the graph. Then move on to describing maximum and minimum points. Which is which? How do you know? Why do you think it is technically called a local maximum and local minimum. For an extension question ask: What is the 3rd type of stationary point? What would it look like? (This is called a point of inflection, which is not covered in the engineering syllabus.)

## Slide 3: Determining stationary points using differentiation
Suppose we want to know where the gradient of the curve is 0. We could look at the graph and estimate this, but this method depends on the complexity of the curve or the accuracy of your graph, so the answers may not be exact.
Alternatively, you can determine stationary points using algebraic methods.
As we are interested in finding the points on the graph where the gradient is 0, we need to determine the gradient function, set it equal to 0 and then solve the resulting equation.

## Slide 4
Let's use the equation from the previous example.
We can now set the differentiated function equal to 0 and solve to determine which values of give a stationary point.
Use the quadratic formula to solve the equation.
Divide each term by 2 to simplify the equation.

## Slide 5
The next step is to determine whether each point identified is a maximum or a minimum.
There are two methods to determine this.

## Slide 6: Method 1 – evaluating gradients
We know that and yield stationary points, so to determine the nature of them we can evaluate using values of on either side of the stationary points.
.125 |  | 
This shows a minimum
This shows a maximum
Notes: Extension question – can anyone spot what may go wrong with this method? Answer: if the values on either side are too far apart, you may miss a stationary point. Demonstrate this using the previous graph and evaluating at x = −1 and x = 1.9.

## Slide 7: Method 2 – using second differentials
Find the second differential.
Substitute your values of into the second differential.
If then it is a minimum.
If then it is a maximum.

## Slide 8
When , therefore, it is a minimum.
When , therefore, it is a maximum.

## Slide 9
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.