## Slide 1: PowerPoint 14: Thermodynamic systems, sensible heat and latent heat
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.8 Thermodynamics in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe types of thermodynamic system (open, closed, temperature, pressure, volume)
explain the meaning of ‘sensible heat’ is and carry out calculations using it
explain the meaning of latent heat of fusion and latent heat of vaporisation and carry out calculations using latent heat.

## Slide 3: Introduction
Thermodynamics is the science of energy changes involving work and heat.
The word ‘thermos’ means heat or energy. The word ‘dynamics’ stands for motion or change.
Together, they mean ‘energy-changes’ or ‘energy-motion’.
The laws of thermodynamics describe these energy changes.

## Slide 4: Thermodynamic systems
You need to be aware of the following types of systems in thermodynamics:
An open system can exchange both energy and matter with its surroundings. Heating a pan on the hob of a cooker is an open system, because heat and water vapour can be lost to the air.
A closed system can exchange only energy with its surroundings, not matter. If we put a very tightly fitting lid on the pan from the previous example, it would approximate a closed system.
In thermodynamics, systems typically involve temperature, pressure or volume (or any combination thereof).

## Slide 5: Sensible heat
Sensible heat is heat that causes a change in the temperature of an object.
The amount of heat energy, Q, required to raise the temperature of a substance depends upon:
  the mass, m
  the specific heat capacity of the substance, c
  the temperature change, t.
The formula is: Q = m c t
The SI unit for quantity of heat is the joule (J).

## Slide 6: Specific heat capacity
The specific heat capacity is the amount of heat required to change a unit mass of a substance by one unit of temperature.
Typical values of the specific heat capacity, c:
Substance | Specific heat capacity J kg−1 oC−1
Water | 4187
Cast iron | 544
Steel | 480
Copper | 385
Aluminium | 921

## Slide 7: Example of sensible heat calculation
Calculate the amount of energy, in megajoules, that is necessary to raise the temperature of 10 kg of steel from 20 to 420 .
The specific heat capacity of the steel is 480 J kg−1 oC−1.
Answer:
Q = m c t
Q = 10 × 480 × (420 – 20)
Q = 1 920 000 J = 1.92 MJ

## Slide 8: Latent heat
Latent heat is the amount of energy needed to change the state of a material.
  For a change from solid to liquid, this is called the specific latent heat of fusion.
  For a change from liquid to vapour, this is called the specific latent heat of vaporisation.
As energy can neither be created nor destroyed, the same amount of thermal energy is released per kilogram when a substance freezes as is required for it to melt, and the same amount of energy is released when it condenses as is required for it to boil.

## Slide 9: Typical values of latent heat
Substance | Specific latent heat of fusion kJ kg−1 | Specific latent heat of vaporisation kJ kg−1
Water | 334 | 2257
Oxygen | ̶ | 243
Aluminium | 9130 | 
Copper | 3850 | 
Steel | 4200 | 

## Slide 10: Formula
The quantity of thermal energy, Q, required to change the state of a substance depends upon:
  the mass, m
  the specific latent heat, h.
The formula is: Q = m h
The SI unit for quantity of energy is the joule (J).
A change of state takes place at a constant temperature.

## Slide 11: Example of latent heat calculation
The specific latent heat required to melt copper is 3850 kJ kg−1.
Find the quantity of latent heat required to melt 15 kg of copper at its melting point.
Answer:
Q = m h
Q = 15 × 3850
Q = 57 750 J = 57.75 kJ

## Slide 12
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.