## Slide 1: PowerPoint 15: Thermal expansivity and heat transfer
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.8 Thermodynamics in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the meaning of thermal expansivity
carry out calculations using thermal expansivity
carry out calculations using the coefficient of heat transfer.

## Slide 3: Thermal expansion
When most materials are heated, they expand – they get bigger in all directions.
As a material cools, it contracts – they get smaller in all directions.
The effect of expansion and contraction depends on:
  the amount of temperature change
  the material.
There are three types of thermal expansion:
  linear expansion
  area expansion
  volume expansion.

## Slide 4: Examples of how thermal expansion affects products
Railway lines that are not fully welded need to have a gap left between the rails. Failure to leave a gap would result in the rails buckling as they expand in hot weather.
Overhead electrical cables hang low in the summer. Without this allowance, as they contract in the winter, they could break.
Bridges are usually designed with one end free and able to move, because the metal in the bridge expands when it is heated.

## Slide 5: Coefficient of linear expansion
The increase in length of a material when its temperature is raised by one degree is called the coefficient of linear expansion.
Coefficient of linear expansion is represented by the Greek letter α.
Units are usually written as K−1.
A change in temperature of 25 K (kelvin) in the same as a change of 25 °C (Celsius), as the same temperature interval is used for both systems.
Note: the kelvin scale is a measure of the absolute temperature; 0 K is equal to −273 °C.

## Slide 6: Coefficient of linear expansion: example
The coefficient of linear expansion of brass is 18×10−6 K−1.
This means that a 1-metre-long brass bar will expand by 0.000 018 m if its temperature is raised by 1 K.
If a 5 m length of brass has its temperature increased by 30 K, it will expand by:
  5 × 0.000 018 × 30 = 0.0027 m or 2.7 mm

## Slide 7: Coefficient of linear expansion: typical values
Material | α (× 10−6 K−1)
Steel | 15
Aluminium | 23
Copper | 17
Brass | 18
Nylon | 100
Acrylic | 71
Glass fibre reinforced epoxy composite | 36
Rubber | 80

## Slide 8: Formula for linear thermal expansion
Original length = l1
Original temperature = T1
Coefficient of expansion = α
New temperature = T2
New length = l2
Increase in length:
Δl = l1 α (T2 − T1)
New length = original length + expansion
l2 = l1 [1 + α (T2 − T1)]

## Slide 9: Example calculation A
A steel pipe is 30 m long at a temperature of 22 °C.
During operation, the temperature of the pipe rises to 300 °C. The value of α for the steel is 16×10−6 K−1.
Calculate the length of the pipe at its operating temperature.
Answer:
l2 = l1 [1 + α(T2 − T1)]
= 30 [1 + (16 × 10−6 )(300 − 22)]
= 30 [1 + (0.000 016)(278)]
= 30 (1.004 448)
= 30.133 m (an increase in length of 133 mm)

## Slide 10: Example calculation B
A bridge is 120 m long at 15 °C.
Its length increases by 90 mm at 65 °C.
Calculate its coefficient of expansion.
Answer:
l2 = l1 [1 + α(T2 − T1)]
120.090 = 120 [1 + α(65 − 15)]
= 120 + 120α × 50
Rearranging: α =
α =
α = 10×10−6 K−1

## Slide 11: Linear expansion
Linear expansion is the change in length due to heat. The formula for linear expansion is
where:
l0 = original length
l = expanded length
αl = length expansion coefficient
ΔT = temperature difference
Δl = change in length

## Slide 12: Area expansion
Area expansion is the change in area due to a change in temperature. The formula for area expansion is
where:
A = original area
ΔA = change in the area
αA = area expansion coefficient
ΔT = temperature difference
A0 = expanded area

## Slide 13: Volume expansion
Volume expansion is the change in volume due to temperature. The formula for volume expansion is
where:
V0 = original volume
V = expanded volume
αV = volume expansion coefficient
ΔT = temperature difference
ΔV = change in volume after expansion

## Slide 14: Heat transfer coefficient
The coefficient of heat transfer through a material is given by
where:
h = heat transfer coefficient (kJ h−1 m−² oC−1)
q = heat flux (W m−²)
Δ T = temperature difference (oC)

## Slide 15: Heat transfer equation
The rate of of heat transfer through a material is given by
Q = heat transfer rate (kJ h−1) = h × A × ΔT
where:
A = Heat transfer area (m²)
h = heat transfer coefficient (kJ h−1 m−² °C−1)
ΔT = temperature difference (°C)
  Example
  Find the heat transfer rate for an application where ΔT = 30 °C, A = 1.2 m2 and the overall heat transfer coefficient is 45 kJ h−1 m−² °C−1.
  Answer: Q = h × A × ΔT = 45 × 1.2 × 30 = 1620 kJ h−1 = 1.62 MJ h−1

## Slide 16
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.