## Slide 1: PowerPoint 4: Measurement
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.4 Measurement equipment, techniques and principles

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the principles of measurement
describe a variety of equipment used for measurement and what they are used to measure.

## Slide 3: Principles of measurement
Precision – measurements should be close to their true values.
Accuracy – the values of measurements should be close to each other (low scatter).
Uncertainty – the statistical dispersion of the values of a measured quantity should be small.
Resolution – this is the ability to detect small changes in the characteristics of the measurement.
Calibration – measurements using a device should be compared with a calibration standard of known accuracy before use.
Tolerance – this is the maximum permissible variation in a measured dimension.

## Slide 4: Measurement devices
Engineering rule
Used to measure linear dimensions
Accurate to approximately 0.5 mm
Vernier caliper
Not as accurate as a micrometer but can be used to measure:
  outside diameter or length
  inside diameter or length
  depth of slot or pocket.
High accuracy to 0.02 mm

## Slide 5: Vernier caliper
Internal jaws
Locking screw
Imperial scale
Metric scale
External jaws
Depth measuring blade

## Slide 6: Example Vernier measurement

## Slide 7: Outside micrometer
Highly accurate to within 0.01 mm
Typically used to measure outside diameters and outside lengths of blocks
Come in various sizes but always with a 25 mm range: for example, 0–25 mm, 25–50 mm, 50–75 mm

## Slide 8: Inside micrometer
Highly accurate to within 0.01 mm
Used to measure inside dimensions such as the inside diameter of a hole or tube
Three types: caliper-type, tubular and bore.

## Slide 9: Depth micrometer
Used to measure the depth of holes, slots, counterbores and recesses
Rods of different sizes can be attached to alter the measurement range
Highly accurate to 0.01 mm
Typical range of 25 mm

## Slide 10: Dial test indicator (DTI)
Extremely accurate to within 0.005 mm.
Uses include:
To check for runout when holding a billet in a lathe.
In a quality environment, to check for flatness of a particular surface.
On the workshop floor, to initially set up or calibrate a machine, prior to a production run.
By toolmakers (mould makers) in the process of manufacturing precision tooling.

## Slide 11: Slip gauges/gauge blocks
Precision ground and lapped measuring blocks.
Used as references for the setting of measuring equipment such as micrometres or dial test indicators (when used in an inspection role).
Used to measure slots and grooves with high accuracy (0.005 mm).
Slip gauges are wrung together to give a stack of the required dimension.

## Slide 12
Using slip gauges correctly
Use the minimum number of blocks possible to measure each dimension.
Wring the individual blocks together.
Wipe the measuring faces clean using soft clean cloth.

## Slide 13: Angle gauges
Precision ground and lapped measuring blocks of hardened steel, typically approximately 75 mm long and 16 mm wide.
They differ from slip gauges in that their wringing surfaces are not parallel to each other, but are at an angle (which is engraved on them).
They can facilitate measurement of any angle between 0 degrees and 360 degrees, with an accuracy of 0.5 to 0.25 second. (1 second = of a minute = of a degree)

## Slide 14: Go/no-go gauge design
The ‘go’ gauge should always be so designed that it will cover the maximum metal condition (MMC – smallest hole, largest shaft), whereas a ‘no-go’ gauge will cover the minimum (least) metal condition (LMC largest hole, smallest shaft) of a feature, whether external or internal.​
​The ‘go’ gauge should always be so designed that it will cover as many dimensions as possible in a single operation, whereas the ‘no-go’ gauge will cover only one dimension.​
For example, this means that a ‘go’ plug gauge should have a full circular section and be of full length of the hole being checked.

## Slide 15: Go/no-go principle

## Slide 16: Go/no-go principle

## Slide 17: Coordinate measuring machine (CMM)
A coordinate measuring machine (CMM) is a device that measures the geometry of physical objects by sensing discrete points on the surface of each object with a probe.
Various types of probes are used in CMMs, including mechanical, optical, laser and white light. Depending on the machine, the probe position may be manually controlled by an operator or it may be computer controlled.
CMMs typically specify a probe's position in terms of its displacement from a reference position in a three-dimensional Cartesian coordinate system (i.e., with xyz axes).

## Slide 18
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.