## Slide 1: PowerPoint 7: Chemical behaviours
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.5 Chemical composition and behaviours

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the types of electrical cells and their characteristics
describe electrolysis
describe the reactions of metals and alloys with acids and alkalis.
Notes: Photo shows electrolysis bathtub with copper anodes at manufacturing plant.

## Slide 3: Batteries and cells
Usually a battery is made up of cells. The cell is what converts the chemical energy into electrical energy.
A simple cell contains two different metals (electrodes) separated by a liquid or paste called an electrolyte.
One metal is more reactive than the other. Negatively-charged electrons flow from the more reactive metal through the wires to the less reactive metal.

## Slide 4: Primary and secondary cells
Primary cell
Primary cells have high power density and get discharged slowly. Since there is no fluid inside these cells they are also known as dry cells. The internal resistance is high and the chemical reaction is irreversible.
Secondary cell
Secondary cells have low energy density and are made of molten salts and wet cells. The internal resistance is low and the chemical reaction is reversible.

## Slide 5: Battery examples

## Slide 6: Primary versus secondary cells
Primary cell | Secondary cell
Have high energy density (cell capacity) | Smaller energy density (cell capacity)
Slow to discharge (output power capacity) | Can be discharged slightly more quickly (higher output power capacity)
There are no fluids in the cells (hence also called dry cells) | These are made up of wet cells (flooded and liquid cells) and molten salt (liquid cells with different composition)
High internal resistance | Low internal resistance
Irreversible chemical reaction | Has a reversible chemical reaction
Initial cost is low | Initial cost is high

## Slide 7: Electrolysis
Ionic substances contain charged particles called ions. For example, lead bromide contains positively charged lead ions and negatively charged bromide ions.
Electrolysis is the process by which ionic substances in a compound become disassociated when an electric current is passed through it.

## Slide 8: The process of electrolysis
For electrolysis to work, the compound must contain ions. An electrolyte is a ionically bonded substance that is either molten or dissolved in water so that the ions are free to move when a current is passed through it. Covalently bonded compounds cannot act as electrolytes because they contain neutral atoms.
This is what happens during electrolysis:
Positively charged ions (cations) move to the negative electrode (cathode) during electrolysis. They receive electrons and are reduced.
Negatively charged ions (anions) move to the positive electrode (anode). They lose electrons and are oxidised.
The cations and anions move through the electrolyte.

## Slide 9: Electroplating
Electroplating is an electrolytic process in which a metal is disassociated from an electrode and deposited over a metallic or non-metallic surface.
Electroplating is usually used to protect the metals from corrosion by atmospheric air and moisture.

## Slide 10: Anodising
The process of deposition of an oxide film on a metal surface by electrolysis is known as anodising.
It is mainly used to increase the thickness of the natural oxide layer on the surface of metallic parts.

## Slide 11: Galvanic protection
Galvanic cathodic protection involves protecting a metal surface of a piece of equipment using another metal that is more reactive.
The coating is the galvanic or sacrificial anode. It has a less negative electrochemical potential compared with the metal component being protected. Therefore, it undergoes oxidation rather than the metal it is protecting.
Sometimes, steels are galvanized rather than connected to galvanic anodes. Galvanized steels are steels that are coated with a protective zinc layer. The zinc layer acts to cathodically protect steel against corrosion.

## Slide 12: Metals and acids
Acids react with some metals to produce a salt and hydrogen gas.
  metal + acid → salt + hydrogen
When a metal is put into acid, it gets smaller and smaller as it gets used up during the chemical reaction that occurs.
At the same time, bubbles of gas can be seen. These bubbles are the hydrogen gas produced in the reaction.
Some metals are very reactive, e.g. potassium. This means they easily take part in chemical reactions to make new substances.
Other metals are very unreactive, e.g. gold, and do not easily take part in chemical reactions.

## Slide 13: Reactivity of metals
Tin, Lead
Copper, Silver, Gold, Platinum
Magnesium, Aluminum
Iron, Zinc
Sodium, Potassium
Calcium
Most reactive
Least reactive

## Slide 14: Reactivity series
Metal | Reaction with dilute acids
Potassium | Violent reaction
Sodium | 
Calcium | Rapid bubbling
Magnesium | 
Aluminum | Rapid bubbling with a slow start
Zinc | 
Iron | Slow bubbling
Tin | 
Lead | Very slow bubbling
Copper | 
Silver | No reaction
Gold | 
Platinum | 

## Slide 15: Alloys and acids
An alloy is a mixture of two or more metals.
Whether an alloy reacts with an acid or alkali depends on what the alloy is made of.
If the alloy mixture contains an element that is more reactive than the other element within the alloy, then the reaction would be less vigorous compared with that of a single element.
Example of alloys include brass, bronze, stainless steel, nickel steel, titanium alloys and aluminum alloys.
Titanium alloy

## Slide 16: High risk operations
Being aware of how metals react with acids and alkalis is important. Many metals are corroded by acids because they react with them to produce hydrogen gas.
Whether or not a particular reaction will occur depends on:
the acid
the metal
whether the acid or alkali is concentrated or dilute.
The hydrogen produced during the reaction between a metal and an acid is lighter than air and is likely to produce a flammable/explosive atmosphere in a confined space.

## Slide 17: Applications
These interactions are widely used in engineering:
Electroplating can be used to improve aesthetics or reduce corrosion.
Galvanic protection can be used to protect metal parts from corrosion.
Chemical etching by reaction with acids or alkalis is used to make markings or create features on metal surfaces by reacting away unwanted material.
Chemical etching is used to make copper traces to connect different components on a circuit board.

## Slide 18: Chemical etching
Chemical etching is also used to change the texture of a surface, for example:
  to increase the roughness of a surface (for aesthetics or grip)
  to improve the effectiveness of bonding
  to facilitate the retention of oils and lubricants.
Conversely, these processes can be used to make a surface less rough, so as to reduce friction and lubrication requirements.

## Slide 19
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.