## Slide 1: PowerPoint 8: Types of motion and forces
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.6 Forces and motion in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the types of motion
calculate force and pressure
define the moment of a force and torque.

## Slide 3: Types of motion
Motion can be described as being of the following types.
Linear
Rotary
Reciprocating
Oscillating
Each type of motion makes use of an applied force (input) to make a movement in a set pattern (output)

## Slide 4: Types of motion
Linear motion involves movement in a straight line, e.g. a train moving along a straight, horizontal track.
Rotary motion occurs when an object moves around an axis or pivot point, e.g. a bicycle wheel.

## Slide 5: Types of motion
Reciprocating motion involves a repeated up and down or back-and-forth movement, e.g. a piston.
Oscillating motion involves a curved backwards and forwards movement that swings on an axis or pivot point, e.g. a swing or a clock pendulum.

## Slide 6: Force
A FORCE is a push or pull exerted by one object on another.
Force is generally recognised and measured by its effect on a body. A force exerted on an initially static body will either move the body or deform it in some way.
The SI unit of force is the newton and is defined as:
1 newton is the force that gives a mass of 1 kg
an acceleration of 1 m s−2
As a force has magnitude and direction, it is a VECTOR quantity.
Weight force F = mg where the acceleration due to gravity, g, is approximately equal to 9.81ms−2.

## Slide 7: Applied forces
Any applied force is called an ACTION and the opposing force is called a REACTION.
Magnitude (size)
Direction
Point of application
A force has 3 defining characteristics:

## Slide 8
Pressure
P =
F
A
Applying a force to any object will create pressure on it, given by
Pressure
(Pa)
Area (m2)
Force (N)
where:
  P = pressure in Pa
  F = force in N
  A = area in m2
Rearranging this gives, A = FP and F = PA

## Slide 9
A force of 400 N is applied to an area of 200 mm2. What is the pressure, measured in bar?
P =
400 N
200 × (1 × 10−6) m2
P = 2 × 106 Pa
P = 2 × 106 N m− 2
P = (2 × 106) × (1 × 10−5) bar
Answer: P = 20 bar
P in Pa =
F in N
A in m2
Area = 200 mm2
Force = 400 N
Pressure = ?
Since 1 Pa = 1 × 10−5 bar:
Example calculation 1

## Slide 10
Example calculation 2
This cylinder is powered by a hydraulic pump producing pressure of 260 000 Pa. What force will the cylinder produce?
F = P × A
A = πr2 = π × (22.5 × 10−3 m)2
A = 1.59 × 10−3 m2
F = 260 000 Pa × 1.59 × 10−3 m2
Force = 414 N (3 significant figures)
Bore diameter = 45 mm
First, find the area:
Insert known values into the equation:

## Slide 11
Example calculation 3
A piece of industrial machinery stands on four feet, one at each corner. Each foot has an area of 900 mm2. The force pushing down on each foot equates to 12 500 N.
What is the pressure on the ground under each foot?
Give your answer in MPa to 1 d.p.
Pressure =
force
area
=
12 500 N
0.0009 m2
Pressure = 13 888 888 Pa = 13.9 MPa (to 3 d.p.)

## Slide 12
A hydraulic system is used to raise a load. The pressure in the system is 1.2 MPa and the piston has an area of 0.0014 m2. What force is produced by the piston?
Give your answer in N.
Force = pressure × area
Force = 1.2 × 106 Pa × 0.0014 m2
Force = 1 680 N
1.2 MPa = 1.2 × 106 Pa
Example calculation 4

## Slide 13
For a lever to balance, the sum of the anticlockwise moments must be equal to the sum of the clockwise moments about any point.
5N
5N
1.5 m
1.5 m
Moments of a force
A moment measures the tendency of a force to rotate a body.
A moment is calculated by multiplying the load (newtons) by the distance from the fulcrum (or pivot) (metres).
The unit of a moment is the newton metre (N m)
Moments are identified as either clockwise or anticlockwise.

## Slide 14: Calculating moments: Example 1
anticlockwise moment = clockwise moment
6 N
A
2.5 m
1.5 m
What value of force A is required to balance this lever?
Rearranging gives A = 15 ÷ 1.5 = 10 N
6 N × 2.5 m = A N × 1.5 m

## Slide 15: Calculating moments: Example 2
anticlockwise moment = clockwise moment
Irrespective of the type of lever, the calculation method is the same.
Calculate the moment and magnitude of force B required to balance this lever.
Force: B N × 2 m = 12 N × 8 m, which gives B = 96 ÷ 2 = 48 N
12 N
B
2 m
8 m
Moment of 12 N force = 12 N × 8 m = 96 N m

## Slide 16: Torque
Torque is a moment that causes rotation about an axis.
A common example of torque occurs when using a spanner.
The torque being applied by the spanner to this nut is calculated in a similar way to the moments in the previous lever examples.
Torque applied = (0.3 × 20) + (0.6 × 10) = 12 N m

## Slide 17
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.