## Slide 1: PowerPoint 9: Vector representation of forces and coplanar forces
PowerPoint presentation
5. Essential science for engineering and manufacturing
5.6 Forces and motion in engineering

## Slide 2: Objectives
By the end of this session, learners should be able to:
carry out calculations using forces represented by vectors
state the conditions for equilibrium
carry out calculations involving coplanar forces.

## Slide 3: A force has magnitude and direction and can be represented graphically in two dimensions as a vector. The length of the line represents the magnitude, and the angle indicates the direction.
Vector representation of force
The force F acts at an angle θ to the horizontal and as such, can be split into a vertical and a horizontal component.
The vertical component = sin θ
The horizontal component = cos θ
Resultant magnitude |F| =

## Slide 4: Resultant angle θ
The angle in which the resultant force is applied can be either measured from the force diagram using a protractor or calculated from the equation below
Resultant angle

## Slide 5: Sign convention
M +
M −
Upward forces are positive (+) and downward forces are negative(−).
Horizontal forces acting to the right are positive(+) and to the left are negative(−).
Clockwise acting moments/couples are positive(+) and anticlockwise ones are negative(−).
+
+
-
-

## Slide 6: Calculate the resultant of the two forces shown.
Force vector example

## Slide 7: Resolving vertical components:
FV = 7 sin 70°+ 5 sin 30°= 9.08 N
Resultant force R = = = 11.3 N
Resultant angle θ =
= 53.5°
Force vector example
Resolving horizontal components:
FH = 7 cos 70°+ 5 cos 30° = 6.72 N

## Slide 8: Equilibrium
Equilibrium means that all forces acting on an object or system are arranged in a way that there is an overall resultant force of zero. This means that there can be no acceleration and so the object must either be static or moving at a constant velocity.
There are several conditions that need to be met in order to bring an object or system into equilibrium:
The sum of the forces in the horizontal direction is zero.
The sum of the forces in the vertical direction is zero.
The sum of all moments is zero.

## Slide 9: Conditions for static equilibrium
An object is in equilibrium if the net forces on it are zero.
This does not mean that there are no forces acting on it – it means that the forces on the object balance out.
Mathematically this is represented as:
ƩFV = 0
ƩFH = 0
ƩM = 0

## Slide 10: Equilibrant force
This is the force that would need to be present in order to bring the system into equilibrium. It would need to be equal in magnitude and opposite in direction to the resultant as shown below.

## Slide 11: Equilibrium conditions
A system with two forces is in equilibrium when:
F1 + F2 = 0, i.e. F1 = −F2.
A system with 3 forces is in equilibrium when:
F1 + F2 + F3 = 0, i.e. F1 = −(F2 + F3).
Trigonometry, Pythagoras’ theorem and vector addition may be needed to calculate the balancing forces.

## Slide 12: Trigonometry and Pythagoras’ theorem
Trigonometry may be required to calculate the angles between force vectors
tan θ =
Rearranging, θ = tan-1
Pythagoras’ theorem (a2 + b2 = c2) may be needed to calculate the magnitude
O
H
A
θ

## Slide 13: Example calculation
A motion-damping system in a machine is at equilibrium when three forces are acting on it:
R N, F1 = (5i – 8j) N and F2 = (3i + 4j) N.
Express R in the form ai + bj.
Answer: Rearranging R + F1 + F2 = 0 gives R = −(F1 + F2)
Therefore R = −((5i – 8j) + (3i + 4j)) = (−8i + 4j) N
Calculate the magnitude of R.
Answer: Magnitude = = = 8.94 N

## Slide 14: Example calculation
c) Calculate the angle that R makes with the i direction.
Answer:
However, the value of the i component of the vector is negative.
Hence, relative to the i direction the angle of the cable, is
(180 + 26.6)o = 206.6o (or −153.4o).

## Slide 15
Coplanar forces
Forces that act within a two dimensional plane are referred to as coplanar forces.
If all of the lines of action of these forces pass through the same point, known as the point of concurrence, then we have a concurrent coplanar force system.
F4
F1
F3
F2
Point of concurrence

## Slide 16: Four coplanar forces act at a point O. The diagram shows the values and direction of the forces.
Calculate the resultant force and describe the magnitude and direction of the force required to bring the system into equilibrium.
Coplanar forces example

## Slide 17
Force (N) | Horizontal component (N) | Vertical component (N)
50 | 50 cos 0o = 50 × 1 = 50 N | 50 sin 0o = 50 × 0 = 0 N
10 | 10 cos 90o = 10 × 0 = 0 N | −10 sin 90o = 10 × 1 = −10 N
20 | −20 cos 30o = −20 × 0.866 = −17.32 N | −20 sin 30o = −20 × 0.5 = −10 N
30 | −30 cos 60o = −30 × 0.5 = −15 N | 30 sin 60o = 30 × 0.866 = 25.98 N
Resultant | 50 – 17.32 – 15 = 17.68 N | −10 − 10 + 25.98 = 5.98 N
Resultant force R
R2 = (17.68)2 + (5.98)2
R =
R = 18.66 N
Coplanar forces example

## Slide 18
The following force is required to bring the system into equilibrium.
Coplanar forces example

## Slide 19
Non-concurrent coplanar force systems
Another type of coplanar system exists where the lines of action of the forces do not pass through the same point. These type of systems are called non-concurrent coplanar force systems.
In this type of system, there is not only a tendency for the force to move the body in a certain linear direction, but also to make it rotate.

## Slide 20
In non-concurrent coplanar force systems, forces in the same plane do not meet at one point.
The resultant force can be calculated in the same way as for concurrent forces.
However, a turning effect occurs as well.
This can be calculated using moments.
F2
F1
F3
F4
Non-concurrent coplanar force systems

## Slide 21: The members in this structure are acted upon by the four forces shown. Determine the magnitude and direction of the resultant force and the perpendicular distance of its line of action from O.
Non-concurrent coplanar force system example

## Slide 22
Force | Angle | FH | FV | MH | MV
4 kN | 40° | 4cos 40 = 3.06 kN | 4sin 40 = 2.57 kN | 0 | 2.57 × 0.25 = −0.64 kN m
7 kN | 180° | 7cos 180 = −7 kN | 7sin 180 = 0 kN | 0 | 0
8 kN | 135° | 8cos 135 = −5.66 kN | 8sin 135 = 5.66 kN | 5.66 × 0.4 −2.26 kN m | 0
Total |  | −9.60 kN | 8.23 kN | −2.90 kN m Anticlockwise | 
Force | Angle | FH | FV | MH | MV
4 kN | 40° | 4cos 40 = 3.06 kN | 4sin 40 = 2.57 kN | 0 | 2.57 × 0.25 = −0.64 kN m
7 kN | 180° | 7cos 180 = −7 kN | 7sin 180 = 0 kN | 0 | 0
8 kN | 135° | 8cos 135 = −5.66 kN | 8sin 135 = 5.66 kN | 5.66 × 0.4 −2.26 kN m | 0
Total |  | −9.60 kN | 8.23 kN |  | 
m
to the horizontal

## Slide 23
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.