## Slide 1: PowerPoint 7: Material structures
PowerPoint presentation
6. Materials and their properties
6.2 Types of material and their structures

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
describe basic atomic structure and the difference between elements and compounds
describe the process of bonding
discuss types of material structure.

## Slide 3: Atomic structure
All materials are formed from atoms which themselves are constructed of three parts.
Proton – positive particle within the atom, forms part of the nucleus.
Neutron – part of the nucleus with no charge.
Electron – negative particle that sits in an orbit around the nucleus.

## Slide 4: Elements and compounds
 | Element | Compound
Definition | Pure substances which are composed of only one type of atom | Substances formed by two or more different elements united chemically in fixed proportions
Total numbers | There are nearly 118 elements (at present) of which nearly 94 occur naturally on Earth (see the periodic table on the slide 6) | Compounds are almost endless
Types | Elements are classified as either metals, non-metals or metalloids | Compounds are classified according to their bonds: ionic, molecular or metallic

## Slide 5: Elements and compounds
 | Element | Compound
Representation | Elements are represented by symbols and numbers. For example, sodium is represented by Na | Compounds are represented by their chemical formulae. For example, salt is represented by the formula NaCl
Ability to break down | Elements cannot be broken down by chemical reactions | Compounds can be easily separated into simpler substances by chemical reactions

## Slide 6: Periodic table

## Slide 7: Atomic bonding
There are three primary types of atomic bonding:
covalent bonding
ionic bonding
metallic bonding.

## Slide 8: Covalent bonding
A covalent bond is formed between atoms of non-metallic elements in which there is a strong attractive force between the nucleus and the outer shell electrons.
This means that instead of a transference of electrons (ionic bond) there is a sharing of electrons between the two atoms that binds them together.

## Slide 9: Ionic bonding (electrovalent bonding)
This type of bond occurs between metals and non-metals. In ionic bonding some of the valence electrons of a metal atom are transferred to a non-metal atom so that each atom ends up with a noble gas configuration. Usually one, two or three electrons are transferred from one atom to another. The image shows this bond in sodium fluoride.

## Slide 10: Metallic bonding
In a metallic bond, metal atoms achieve a more stable configuration by sharing the electrons in their outer shell with many other metal atoms. The valence electrons in metals are not tightly bound in the nucleus and each atom in a metal contributes all the electrons in its valence shell to all the other atoms in the structure.

## Slide 11: Van der Waals bonds
Van der Waals bonds occur to some extent in all materials but are particularly important in plastics and polymers. These materials are made up of a long string molecules consisting of carbon atoms covalently bonded with other atoms, such as hydrogen, nitrogen, oxygen and fluorine.
The covalent bonds within the molecules are very strong and rupture only under extreme conditions. The bonds between the molecules that allow sliding and rupture to occur are called van der Waals forces.

## Slide 12: Van der Waals forces
Van der Waals forces are short-range forces existing in both gas and liquid phases due to the fluctuation in electron clouds surrounding the nucleus, which can be determined by London–van der Waals theory (microscopic theory) or Lifshitz–van der Waals theory (macroscopic theory).

## Slide 13: Material states
All metals and other materials can exist as gases, liquids or solids.
The state in which a metal exists depends upon the conditions of temperature and pressure that exist at the time.
Depending on the process, the atoms arrange themselves according to some regular pattern or lattice structure.

## Slide 14: Structure of polymers
A polymer is composed of many simple molecules that are repeating structural units called monomers.
A single polymer molecule may consist of hundreds to a million monomers and may have a linear, branched or network structure.
Covalent bonds hold the atoms in the polymer molecules together and secondary bonds then hold groups of polymer chains together to form the polymeric material.
Copolymers are polymers composed of two or more different types of monomer.
Notes: Image from
https://www.shutterstock.com/image-vector/polymerization-reaction-polymer-units-how-does-1941189394

## Slide 15: Polymer types

## Slide 16: Structure of ceramics
The atomic bond arrangements of ceramic materials are predominately ionic and covalent. These atomic bonds are much stronger compared to comparable metallic bonds.
This is the main reason why ceramic materials’ hardness values are superior over those of metals.
All the electrons in a ceramic atomic structure are held strictly. Because of this, ceramics are electrically insulative materials.
Generally, ceramic materials have a crystalline structure like most metals, with the atoms firmly held in place, but ceramics can also have an amorphous structure in which the atomic bonds are much weaker.

## Slide 17: Crystalline vs amorphous solids
A crystalline solid or structure is that in which the constituent particles are arranged in a three-dimensional pattern called the crystal lattice, with uniform intermolecular forces. The particles intersect at angles characteristic of the crystal.
An amorphous solid or structure has a shapeless, disordered and irregular arrangement of the constituent particles of a solid. Intermolecular forces are not the same, nor are the distances between the particles.
Notes: Image from
https://www.shutterstock.com/image-vector/illustration-chemical-solid-crystal-structures-arrangement-1732938128v

## Slide 18: Crystalline and amorphous structures
Amorphous structure
Crystalline structure

## Slide 19: Key features of crystalline and amorphous structures
Crystalline
            Ordered alignment, tightly bound, uniform intermolecular force, repeated pattern, geometric shape.
Amorphous
            Random alignment, loosely bound, no defined edges, non-crystalline structure.

## Slide 20: Structure of composites
A composite is made by physically combining two or more materials (components) to produce a combination (blend) of structural properties not present in any individual component.
Composite materials are said to have two phases. The dispersed phase is the fibres, sheets or particles that are embedded in the matrix or continuous phase. The material that is distributed through the matrix is known as the reinforcing phase if it adds strength to the composite.
The reinforcing material and the matrix material can be metal, ceramic or polymer.

## Slide 21: Fibre reinforced polymer composites
Fibre reinforced polymer composites (FRPs), also known as polymer matrix composites (PMCs) are subdivided into the following.
a) Carbon fibre reinforced polymer composites (CFRPs).
b) Glass fibre reinforced polymer composites (GFRPs).
c) Aramid fibre reinforced polymer composites (AFRPs).
In each case the fibre is encased in a resin matrix (the continuous phase). These matrices are usually acrylicepoxyphenolic or polyester resins.

## Slide 22: Particle reinforced composites (PRCs)
Particle reinforced composites (PRCs) are essentially two types of particle reinforced composite: large particle reinforced and small particle reinforced.
In a small particle reinforced material the mechanism is on a molecular level and the particles may be dispersed into or precipitated from the matrix.
Large particle reinforcement involves larger particles and a distribution of the load between phases. Whatever their geometry, the particles are small relative to the size of the structure and evenly distributed through it.

## Slide 23: Composite laminate
A composite laminate is an assembly of layers of fibrous composite materials which can be joined to provide the required engineering properties.
Notes: Images show honeycomb composite panels which have many engineering uses, including in aircraft, and a carbon fibre bespoke car bonnet and vent.
https://www.shutterstock.com/image-photo/honeycomb-composite-panels-repair-station-aircraft-742368391
https://www.shutterstock.com/image-photo/carbon-fibre-bonnet-vent-scoop-1760665802

## Slide 24
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.