## Slide 1: PowerPoint 4 : Conservation of momentum and energy
7. Mechanical principles
7.1 Principles of motion and mechanics in engineering and manufacturing systems
7.2 Principles of forces and energy

## Slide 2: Objectives
By the end of this session, learners should be able to:
calculate linear acceleration
describe the principles of conservation of momentum and the conservation of energy
carry out calculations using potential and kinetic energy.

## Slide 3: Linear acceleration
Acceleration is the measure of how quickly the velocity of any moving object changes. Linear acceleration is acceleration in a straight line.
An object that is moving in a straight line accelerates if its velocity is increasing or decreasing during a given period of time. Acceleration can be either positive or negative depending on whether the velocity is increasing (+) or decreasing (−).
Acceleration is the rate of change of velocity.
It is a vector quantity, so has magnitude as well as direction.
A moving object can accelerate if its speed (the magnitude of the velocity) remains constant but the direction of motion changes.

## Slide 4: Calculating linear acceleration
Acceleration is denoted by the symbol , and calculated using:
The units are metres per second squared or ms−2. If the acceleration is constant, then the equations linking (time taken), (initial velocity), (final velocity), (acceleration) and (displacement) are:
Symbol | Meaning
 | Final velocity
 | Initial velocity
 | Acceleration
 | Time taken
 | Displacement
Symbol | Meaning
 | Final velocity
 | Initial velocity
 | Acceleration
 | Time taken
 | Displacement

## Slide 5: Example 1
A car accelerates from a speed of 3m/s to a speed of 5m/s in 5 seconds.
What is the acceleration?
Given parameters:
        Initial velocity, = 3m/s
        Final velocity, = 5m/s
        Time taken, = 5 seconds
        Acceleration

## Slide 6: Example 2
A stone is released into a river from a bridge. It takes 4 seconds for the stone to touch the river’s surface. Calculate the height of the bridge from the water level.
Initial velocity, = 0 (because the stone was at rest)
Time taken, = 5s
= = 9.8m/s2 ( is acceleration due to gravity because the stone is in freefall)
Displacement of the stone (the height of the bridge),

## Slide 7: Solution
The height of the bridge is found using:

## Slide 8: Conservation of momentum
Two of the most fundamental and useful laws of physics are the principles of conservation of energy and conservation of momentum. They aid in the solution of many mechanical problems identified in different fields of science.
Conservation of momentum describes the state where, if a body has no net external forces acting on it, the total momentum is the same at all times (ie momentum is conserved).
In addition, in a system – for example when two bodies (objects) collide – the amount of momentum lost by one body is equal to the amount of momentum gained by the other.

## Slide 9: Calculating momentum
Mass () is measured in kilograms (kg).
Velocity () is measured in metres per second (m/s).
Momentum () is measured in kilogram metres per second (kg m/s).
A lorry has a mass of 7000kg. It travels at a speed of 30m/s. What is its momentum?
Momentum = mass × velocity

## Slide 10: Conservation of energy
Energy can be transferred, stored or dissipated, but it cannot be created or destroyed. Energy comes from one store and is transferred to another store. All the energy from the ‘Big Bang’ will still exist in the universe until the end of time.
For example, an object falling from a crane transfers its gravitational potential energy store into kinetic energy as its speed increases. Some energy is transferred to the air particles as the object falls, which increases their thermal energy.
The battery of your mobile phone (chemical energy store) loses energy, but this is transferred into light, sound and thermal energy.

## Slide 11: Potential energy
Potential energy (PE) is the energy that an object possesses due to its position.
It can also be energy resulting from internal stresses or electric charge.
PE = mgh, where m = mass of the object, g = gravity and v = velocity.
  Example
  A box of mass 25kg is on a shelf 2m above the ground. Calculate the potential energy of the box.
  Answer: PE = mgh = 25 x 9.8 x 2 = 490J

## Slide 12: Kinetic energy
Kinetic energy is the energy of motion.
An object that has motion – whether it is vertical or horizontal motion or in any other direction – has kinetic energy.
You need to know about two forms of kinetic energy:
translational (the energy due to motion from one location to another)
rotational (the energy due to rotational motion).
Notes: Rotational kinetic energy is covered in a later presentation.

## Slide 13: Translational kinetic energy
Kinetic energy is the energy that an object possesses due to motion.
KE = ½mv2, where m = mass of the object and v = velocity.
  Example
  A machine is ejecting parts after processing. Each part has a mass of 1.2kg and a velocity on leaving the machine of 2m/s-1.
  Calculate the kinetic energy of one part as it leaves the machine.
  Answer: KE = ½mv2 = 0.5 x 1.2 x 22 = 2J

## Slide 14: Conservation of momentum
The principle of conservation of momentum can be applied to bodies colliding so that specific details after collision (or before) can be found.
Consider two bodies A and B of masses m1 and m2, moving with velocities u1 and u2 on a direct collision course.
After collision the two bodies are combined as a single body with velocity u3.
Assuming no losses of energy due to the collision:
m1u1 + m2u2 = (m1+m2) x u3

## Slide 15: Example calculation
Car A of mass 1200kg is travelling with a velocity of 30km hr-1.
It collides a car B of mass 1,600kg travelling with a velocity of 10km hr-1 in the opposite direction.
Assuming that no energy is lost in the collision and the cars can be treated as a single body after the collision, find the final velocity of combined cars.
Answer
m1 = 1200kg, u1 = 30km hr-1, m2 = 1500kg
u2 = -10km hr-1, (negative as moving in the opposite direction)
Rearranging m1u1 + m2u2 = (m1+m2) x u3 , u3 = m1u1 + m2u2 / (m1+m2)
u3 = ((1200 x 30) + (1,600 x 10)) / (1200 + 1600)
u3 = 18.6km hr-1 (to three single figures)

## Slide 16
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.