## Slide 1: PowerPoint 6: Force and resistance in practical applications
PowerPoint presentation
7. Mechanical principles
7.2 Principles of forces and energy

## Slide 2: Objectives
By the end of this session, learners should be able to carry out calculations involving:
gravitational force
frictional resistance.
Learners should also be able to explain and give examples of:
tractive effort
braking force
rotational kinetic energy
moment of inertia
spring force.

## Slide 3: Gravitational force
Gravity is a non-contact force. It is the force with which the earth, moon or any other massively large object attracts another object towards itself. This is the weight of the object. All objects on earth experience a force of gravity that is directed ‘downward’ towards the centre of the planet. The force of gravity on earth is always equal to the weight of the object as found by the equation:
W = mg
where g is approximately – 9.81m/s2 (on earth)
and m = mass (in kg)

## Slide 4: Falling objects and freefall
Freefall refers to a situation in physics where the only force acting on an object is gravity.
The motion of a body falling freely because of the gravitational pull of the earth will be subject to the acceleration due to gravity.
An object that starts from rest and falls freely will follow the three equations of motion under gravity:
h = gt² v² = 2gh v = gt
where h is the vertical displacement, v is the final velocity and g is the acceleration due to gravity.

## Slide 5: Example
Calculate the initial height above the ground of a body of mass of 2kg which reaches the ground after falling vertically for 5 seconds.
Use
h = gt²
Substituting the known values gives:
    h = × 9.8 × 52
    = 4.9 × 25
    = 122.5m

## Slide 6: Frictional resistance
Frictional resistance is the force exerted by a surface as an object moves across it or makes an effort to move across it.
Types of friction force include sliding, rolling and static friction.
Friction force often opposes the motion of an object.
Different surfaces produce different amounts of frictional resistance – for example, you need to push a box harder to get it moving on a carpet than on a wooden floor because there is more friction between the carpet and the box than between the wood and the box.

## Slide 7: Calculating friction
Friction results from two surfaces being pressed together closely, causing intermolecular attractive forces between the molecules of different surfaces.
As such, friction depends on the nature of the two surfaces and on the degree to which they are pressed together.
The maximum amount of friction force that a surface can exert on an object can be calculated using the formula:
Fmax = µ × normal reaction
Fmax = µ ×R

## Slide 8: Tractive effort
This term is often used for the linear force applied to a wheel, which can be either a pushing or a pulling force. The tractive effort between a car wheel and the surface of the road can be expressed as:
F = μt W
= μt mg
F = traction effort or force acting on the wheel from the surface (N)
μt = traction (or friction) coefficient between the wheel and the surface
W = weight or vertical force between wheel and surface (N)
m = mass of the wheel (kg)
g = acceleration due to gravity (9.81m/s2)

## Slide 9: Braking force
Also known as brake power, braking force refers to the total force exerted on a moving body that causes it to slow to a halt. If the body (vehicle or machinery) is travelling at a known velocity, then this force can be calculated.
Fbraking = ma =
where:
Fbraking = total braking force (N)
m = total vehicle mass (kg)
a = deceleration (m/s2)
= initial velocity (m/s)
= final velocity (m/s)

## Slide 10: Calculating braking force
If a vehicle of mass 1600kg is initially travelling at 90km/h, calculate the braking force required for the car to come to a complete stop in 50m.
1600kg
Work done = loss in KE = braking force ×distance
Braking force =

## Slide 11: Rotational kinetic energy
Any rotating object has rotational kinetic energy. For example, flywheels are used as a means of temporarily storing energy by rotating.
The amount of rotational kinetic energy a body has depends on its moment of inertia (rotational mass) and its angular velocity. It is calculated in a similar way to translational kinetic energy.
The moment of inertia measures how difficult it is to change the rotational motion of a body about an axis. It depends on the mass and how it is distributed.
Each point on a rigid body has a different linear velocity when it rotates. However, we can use angular velocity – which is the same for the entire rigid body – to express the kinetic energy of a rotating object.

## Slide 12: Rotational kinetic energy
Remember: translational kinetic energy is given by
Every point on a rigid body rotating about an axis moves with a different linear velocity, but the rotational kinetic energy can be written in terms of the angular velocity, ω, which is the same for all points on the body, and r, the distance of each point from the axis of rotation. For each point:

## Slide 13: A new variable
Comparing the equation for rotational kinetic energy with the equation for translational kinetic energy
suggests a new variable to describe the relationship between rotational and translational kinetic energy.
The quantity is the counterpart for mass in the equation for rotational kinetic energy. This is an important variable for rotational motion. It is called the moment of inertia, I, and has units kg m2.

## Slide 14: Moment of inertia
The moment of inertia is the quantitative measure of rotational inertia, just as mass is the quantitative measure of linear inertia in translational motion.
The more massive an object is, the more inertia it has, and the greater is its resistance to a change in linear velocity.
Similarly, the greater the moment of inertia of a rigid body or system of particles, the greater is its resistance to a change in angular velocity about a fixed axis of rotation.
Substituting I into the equation for kinetic energy of a rotating rigid body gives:

## Slide 15: Example
Moment of inertia of a system of particles
Six small washers are spaced 10cm apart on a rod of negligible mass and length 0.5m. The mass of each washer is 20g. The rod rotates about an axis located at 25cm from the outermost washers, as shown on the next slide.
What is the moment of inertia of the system?
If the two washers closest to the axis are removed, what is the moment of inertia of the remaining four washers?
If the system with six washers rotates at 5rev/s, what is its rotational kinetic energy?

## Slide 16: Solution
a.
b.
c.
5cm
5cm

## Slide 17: Spring force
Spring force is the force exerted by a compressed or stretched spring on any object that is attached to it. An object that compresses or stretches a spring is always acted upon by a force that restores the object to its rest or equilibrium position.
For most springs (those that obey Hooke’s law), the magnitude of the force is directly proportional to the amount of stretch (extension) or compression of the spring.
Fspring = kx
where k is the spring constant and x is the extension or compression.

## Slide 18
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.