## Slide 1: PowerPoint 6: Power sources
PowerPoint presentation
7. Mechanical principles
7.2 Principles of forces and energy

## Slide 2: Objectives
By the end of this session, learners should be able to explain the function and relative advantages of alternative power sources and give examples of their use, including:
fossil fuel
nuclear
solar
hydro
wind
geothermal
biofuel
mechanical motors.

## Slide 3: Power sources
Power sources can be classified in different ways.
Renewable power sources are naturally replenishing and can be used indefinitely. These are different from non-renewables such as fossil fuels, which will eventually run out.
Electrical power sources generate other forms of energy into electrical energy. This may be by direct conversion (eg solar power), by turning a generator (eg wind/hydropower) or by heating water into steam to power a generator (eg fossil fuels, nuclear, geothermal and biofuels).
Mechanical power sources convert energy into a usable form of motion. These include the internal combustion engine and the electric motor.

## Slide 4: Non-renewable sources of energy
Oil, coal and natural gas are fossil fuels. These are non-renewable energy sources, formed when prehistoric plants and animals died and were gradually buried by layers of rock. Over millions of years, different types of fossil fuels formed – depending on what combination of organic matter was present, how long it was buried and what temperature and pressure conditions existed as time passed.
The main advantages of fossil fuels include a high energy density, existing infrastructure and ease of transportation.

## Slide 5: Oil and gas extraction
Oil is extracted from the ground by drilling, after which the oil is pumped out. There are underground reserves of oil but extraction means depletion. Extracted crude oil is subjected to a heating process to produce fuel for vehicles and other useful products.
Another extraction method is fracking. Scan this QR code to read a BBC article about this method.
Gas may also be found when extracting oil and is extracted from the same site.
Notes: The article linked to the QR code can also be viewed here: http://www.bbc.co.uk/news/business-40580058.

## Slide 6: Natural gas extraction
Notes: Image source: https://www.eia.gov/kids/energy-sources/natural-gas/.

## Slide 7: Gas extraction
In general, gas is extracted in a similar way to oil, by drilling.
Another method of gas extraction is known as ‘fracking’ – the process of drilling into the earth and directing a high-pressure mixture of water, sand and chemicals at a rock layer in order to release the gas inside.
Wells can be drilled vertically or horizontally. The term fracking (derived from the word ‘fracturing’) refers to how the rock is fractured apart by the high-pressure mixture.

## Slide 8: Coal extraction
Coal is mined in two ways.
Surface mining – coal near the surface is dug up and then blasted via a controlled explosion to extract deeper.
Underground mining – coal underground is drilled and extracted.

## Slide 9: Nuclear energy
Nuclear power is not renewable energy but is a zero-emission clean energy source. Sustained nuclear fission can generate heat and electricity. Fission is a reaction in which a heavy nucleus splits spontaneously or on impact with another particle, resulting in the release of large amounts of energy. Radioactive particles are also produced as a byproduct, which need to be managed (kept safe) over extremely long periods of time. The fuel used is uranium, a radioactive element.
At the end of 2021, nuclear energy contributed 16% of the UK’s electricity from 13 reactors. The main advantage of nuclear energy is that is offers a consistent supply of electricity.

## Slide 10: How nuclear energy is generated

## Slide 11: The future of nuclear energy
Scan this QR code to discover more about the UK’s fusion technology.
In the future, it is possible that nuclear fusion (the fusing together of small atoms) may be used to generate energy.
Although the process requires more energy to operate, it also produces three to four times more energy than fission and results in less radioactive waste.
Notes: The article linked to the QR code can also be viewed here: https://ccfe.ukaea.uk/fusion-energy/how-fusion-works/

## Slide 12: Renewable energy sources
Solar.
Wind.
Hydro (water).
Geothermal.
Biofuel.
The main advantages of renewable energy sources are that they are naturally replenished and do not contribute to global warming. With many of these approaches, energy can also be generated locally to where it is required.

## Slide 13: Solar energy
Solar photovoltaic (PV) energy is the fastest growing and most affordable source of new electricity. As the cost of solar energy systems has fallen, more people and businesses have taken advantage of ‘clean’ energy. In 2021, solar energy provided 4% of the UK grid supply.

## Slide 14: How solar panels work

## Slide 15: Wind energy
Wind turbines capture wind power and convert it into electricity. Turbines are often located offshore, but can also been found inland at suitable locations.

## Slide 16: Hydroelectric energy
Hydropower is the use of moving water to produce electricity or to drive machines. The principle is simple: use the power of a moving liquid to turn a turbine blade.
The water is collected in a dam or via a diversion structure to alter the natural flow of a river or other body of water. Water is released to flow over a turbine which then turns a generator to produce electricity. Water mills are based on the same principle, in their case, using the power to drive a machine.

## Slide 17: The Archimedes screw
Small-scale hydroelectric plants can generate energy using the ancient invention of the Archimedes screw.
The screw acts as a positive-displacement pump, lifting water upwards. Such screws can operate in rivers with a relatively low flow, and can work using a low head (the drop between where the water enters the turbine and where it leaves), making them well suited to smaller installations.

## Slide 18: Geothermal energy
Geothermal energy is heat derived from within the earth’s sub-surface which can be harnessed to generate clean, renewable energy. Water and/or steam carry the geothermal energy to the earth’s surface.
Geothermal energy supplies renewable power around the clock and emits little or no greenhouse gases – only a small environmental footprint is produced when these sites are developed. Geothermal energy can be used for heating and cooling purposes or can be harnessed to generate clean electricity.
However, for electricity generation, high or medium temperature resources are needed, which are usually located close to tectonically active regions.

## Slide 19: How geothermal energy generation works

## Slide 20: Bioenergy: biomass and biofuels
Biomass is an organic renewable energy source that uses organic materials from agriculture and forest waste, sewage and algae. Scientists and engineers are finding new, more efficient ways to convert biomass into biofuels that can substitute for conventional fuels such as petrol, diesel and jet fuel.
Biogas plant (left).
Biofuel pellets, which can be used as a heat source (right).

## Slide 21: Mechanical power sources: the internal combustion engine
The internal combustion engine (ICE) relies on fossil fuels. The ICE was perfected by Nicolaus Otto in the 1870s and represented a significant contribution towards industrial development.
The ICE works by igniting fuel (eg petrol) mixed with air inside a chamber. The expansion of the high-temperature and high-pressure gases produced by combustion applies direct force to pistons (piston engine), turbine blades (gas turbine), a rotor (Wankel engine) or a nozzle (jet engine).
This process transforms chemical energy into kinetic energy, which is used to propel, move or power whatever the engine is attached to (eg a car).

## Slide 22: How an internal combustion engine works

## Slide 23: Electric motors
An electric motor converts electrical energy into mechanical energy.
Most electric motors operate through the interaction between the motor’s magnetic field and an electric current in a wire winding, to generate force in the form of torque applied on the motor's shaft.
Electric motors can be powered by direct current (DC) sources (eg batteries), or by alternating current (AC) sources (eg the power grid). They are widely used in engineering in cars, fans, pumps and industrial equipment (eg lathes, winches, hoists and robots).

## Slide 24
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.