## Slide 1: PowerPoint 5: Open and closed loop systems
PowerPoint presentation
Engineering and manufacturing control systems
10.1 Principles and applications of control system theory

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain open and closed loop systems
describe how these systems are represented on engineering drawings.

## Slide 3: Open and closed loop systems
Open loop systems do not have a feedback loop.
Closed loop systems have at least one feedback loop.
Feedback is where the output signal from a system becomes an input signal to the same system. For example:
Process
Output
Input
Feedback

## Slide 4: Open loop or closed loop?
Closed loop systems are more robust as they are less likely to be affected by external disturbances or noise.
Closed loop systems are extremely accurate.
Open loop systems are less complicated and therefore easier to design and maintain.
Open loop systems are less costly to produce as they have less components.

## Slide 5: Applications of open and closed loop systems
Typical applications of open loop systems
  Simple timer and latching systems.
  Simple electronic counters.
Typical applications of closed loop systems
  Temperature control and heating systems.
  Automatic security lighting systems.
  Robotic arms and/or vehicles.
  Can you think of any other examples?

## Slide 6: Transfer functions and summing points
A transfer function is a mathematical representation of the contents of each block within a systems diagram (eg G(s) and H(s) shown below).
The summing point produces the algebraic sum of the reference input signal R(s) and feedback signal B(s), resulting in the error signal E(s). C(s) is the output signal.
G(s)
+
-
R(s)
E(s)
B(s)
C(s)
H(s)

## Slide 7
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.