## Slide 1: PowerPoint 6: Signals
PowerPoint presentation
Engineering and manufacturing control systems
10.1 Principles and applications of control system theory

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the difference between analogue and digital signals
describe pulse width and pulse amplitude modulation.

## Slide 3: Signals
Control systems make use of a range of different types of electrical and electronic signals. These can include voltages, currents and logic states.
  Signals can be either analogue or digital.
  They are usually displayed as waveforms of the change in parameter over time.
  They can be manipulated, modulated or processed for different functions and applications.

## Slide 4: Analogue and digital signals
  Analogue signals transmit information as a continuous set of values.
  Analogue signals are shown as sinusoidal waves. For example, radio waves.
  Digital signals transmit information as a sequence of discrete values (eg 1s and 0s).
  Digital signals are finite.
  Digital signals are shown as square waves.

## Slide 5: Analogue or digital?
Analogue signals are higher density than digital signals and so present more detailed and accurate information.
Analogue signals are more likely to suffer from the effects of noise.
Digital signals take up less bandwidth as they carry less information.
Digital signals are easier to understand, transmit and decode as they can only be one of two values (high or low, 1 or 0).
What other advantages and disadvantages do you think there are for each signal type? Which applications is each best suited for?

## Slide 6: Pulse width modulation
Modulation is where data is converted into electrical signals that are suitable for transmission. For example, radio waves.
Pulse width modulation (PWM) is where the width of the pulsed carrier signal is varied according to the amplitude of the message signal.

## Slide 7: Pulse amplitude modulation
Pulse amplitude modulation (PAM) is where the amplitude of the pulsed carrier signal is varied according to the amplitude of the message signal.

## Slide 8
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.