## Slide 1: PowerPoint 1: Health and safety in engineering
PowerPoint presentation
12. Health and safety principles and coverage
12.1 The main requirements of key health and safety legislation applicable to engineering activities

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
identify the need for health and safety legislation for protecting the workforce and members of the public while working in the engineering and manufacturing industries
explain why there is legislation to cover every aspect of the workplace
describe how such legislation keeps people safe in the workplace
define who is responsible for compliance with current regulations and legislation
appreciate health and safety culture, and be aware of the availability of training and information.

## Slide 3: Why is there a need for health and safety legislation?
Health and safety legislation is wholly about promoting good practice.
Health and safety ensures that the risk of a serious incident is minimised within an organisation.
On average, over 200 people are killed a year in an accident at work and over 1 million are injured.

## Slide 4: Heath and safety statistics
The Health and Safety Executive (HSE) statistics for Great Britain (2020/2021, www.hse.gov.uk/statistics/) showed that:
142 workers were killed at work
441,000 working people sustained an injury at work
51,211 injuries to employees were reported under the Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR).

## Slide 5: Health and safety publications
Health and safety publications can be divided into two distinct groups: mandatory (must be followed by law) and advisory (guidance which is recommended but not legally enforceable).
  Acts of Parliament are also known as statutory legislation. Such acts create a new law or change an existing one. Their implementation is the responsibility of a specific government department. In the case of health and safety, this is the HSE. Acts are legally enforceable and must be followed to avoid prosecution.
  Non-statutory legislation refers to rules, procedures and administrative codes set by authorities or government agencies to achieve a particular objective.

## Slide 6: Health and Safety at Work Act (HASAWA) 1974
The main objectives of HASAWA are:
  the health and safety of all people at work
  the protection of others from risks at work
  the control of dangerous substances
  the control of dangerous emissions.
The full act can be found here: Health and Safety at Work Act 1974 (legislation.gov.uk)

## Slide 7: HASAWA
  The act makes health, safety and welfare everyone’s responsibility.
  Employers have a responsibility to provide personal protective equipment (PPE) (eg hard hats, gloves, eye protection, safety footwear etc).
  A health and safety policy must be produced if a company employs five or more employees.

## Slide 8: Regulations governing engineering and manufacturing
Under HASAWA, a range of regulations apply to the engineering and manufacturing sectors, and you should be aware of these. Health and safety legislation has been developed in an attempt to cover every relevant aspect of work. The list continues on the next slide.
Management of Health and Safety at Work Regulations (MHSWR) 1999
Provision and Use of Work Equipment Regulations (PUWER) 1998
Personal Protective Equipment at Work Regulations 1992
Control of Noise at Work Regulations 2005
Manual Handling Operations Regulations (MHOR) 1992

## Slide 9: Regulations governing engineering and manufacturing
Lifting Operations and Lifting Equipment Regulations (LOLER) 1998
Work at Height Regulations (WAHR) 2005
Electricity at Work Regulations
Control of Electromagnetic Fields at Work Regulations (CEMFAW) 2016
Reporting of Injuries, Diseases and Dangerous Occurrences Regulations (RIDDOR) 2013
Control of Substances Hazardous to Health Regulations (COSHH) 2002

## Slide 10: MHSWR
MHSWR (1999) was introduced to reinforce HASAWA (1974). The regulations explicitly outline what employers are required to do to manage health and safety, and they apply to every work activity. The regulations place a set of duties on employers and employees to maintain a safe and healthy workplace.
Employers must:
undertake risk assessments
appoint a competent person to oversee health and safety
provide health and safety training.

## Slide 11: MHSWR
Employees must:
report any health and safety shortcomings
report dangerous situations as well as incidents and accidents
use equipment in accordance with training and instruction
take care of own health and safety and the safety of others affected by their work.
Management of Health and Safety at Work Regulations 1999 (legislation.gov.uk)

## Slide 12: PUWER
PUWER places duties on people and companies who own, operate or have control over work equipment. For example, the regulations require that equipment provided for use at work is:
used by persons who are trained and competent
effectively guarded to protect the user
maintained, and full records kept.
A guide to PUWER can be found here: Provision and Use of Work Equipment Regulations 1998 (PUWER) (hse.gov.uk)

## Slide 13: PUWER
These regulations require that equipment provided for use at work is:
  suitable for the intended use
  safe for use, maintained in a safe condition and inspected to ensure it is correctly installed and does not subsequently deteriorate
  used only by people who have received adequate information, instruction and training
  accompanied by suitable health and safety measures, such as protective devices and controls – these will normally include guarding, emergency stop devices, adequate means of isolation from sources of energy, clearly visible markings and warning devices
  used in accordance with specific requirements.

## Slide 14: Personal Protective Equipment at Work Regulations
Wherever there are risks to health and safety that cannot be adequately controlled in other ways, the PPE regulations require PPE to be supplied by the employer to the employee. The regulations also require that PPE is:
properly assessed before use to make sure it is fit for purpose
maintained and stored properly
provided with instructions on how to use it safely
used correctly by employees.
A guide to these regulations can be found at: Personal Protective Equipment at Work Regulations from 6 April 2022 (hse.gov.uk)

## Slide 15: Examples of common PPE

## Slide 16: Control of Noise at Work Regulations
The aim of these regulations is to ensure that workers’ hearing is protected from excessive noise at their place of work, which could cause them to lose their hearing and/or to suffer from tinnitus (permanent ringing in the ears).
Employers must provide hearing protection and hearing protection zones if employees are exposed to daily or weekly noise of 85 decibels and above.
The level at which employers must assess the risk to workers’ health and provide them with information and training is 80 decibels.
The full regulations can be found here: Control of Noise at Work Regulations 2005 (legislation.gov.uk)

## Slide 17: MHOR
MHOR 1992 was amended in 2002. The regulations cover the following activities: lifting, lowering, pushing, pulling, moving or carrying a load.
  Individuals should conduct a risk assessment first. Lifting operations should be planned in advance. Employees have a responsibility to use mechanical aids as required in order to avoid injury.
  The regulations can be found in full here: Manual Handling Operations Regulations 1992 (legislation.gov.uk)

## Slide 18: LOLER
Employers are responsible for any lifting equipment they use.
All lifting operations involving lifting equipment must be properly planned by a competent person, appropriately supervised and carried out in a safe manner.
Lifting equipment is work equipment, so PUWER applies here:
inspection, maintenance and records kept
statutory periodic ‘thorough examination’.
Lifting Operations and Lifting Equipment Regulations 1998 (legislation.gov.uk)

## Slide 19: WAHR 2005
Working at height means working in any location where, if there were no precautions in place, a person could fall a distance liable to cause personal injury.
The following will mitigate against falling from height:
guards and fall arresters
harnesses
planning of work
risk assessment
equipment inspections.
Work at Height Regulations 2005 (legislation.gov.uk)

## Slide 20: Electricity at Work Regulations
The ​Electricity at Work Regulations apply to all aspects of the use of electricity within the workplace. Employers must:
have electrical systems constructed in a way that prevents danger
maintain electrical systems as necessary to prevent danger (including a five-year fixed installation inspection​)
carry out work on electrical systems in a way that prevents danger.
Electricity at Work Regulations 1989 (legislation.gov.uk)

## Slide 21: Electricity at Work Regulations
Under the Electricity at Work Regulations, employees should only work on or with electrical equipment if they have suitable:
training
knowledge
experience
supervision.

## Slide 22: CEMFAW
The employer must make a suitable and sufficient assessment of the levels of electromagnetic fields (EMFs) to which employees may be exposed. The CEMFAW regulations contain a schedule which introduces EMF limits, explains the effects of EMFs and provides details of safety conditions which must be met.
EMFs such as x-rays, gamma rays and higher energy untraviolet (UV) rays are emitted by some engineering testing equipment, so knowledge of CEMFAW is important.
Control of Electromagnetic Fields at Work Regulations 2016 (legislation.gov.uk)

## Slide 23: RIDDOR
RIDDOR is a piece of health and safety legislation that was updated in 2013. This introduced significant changes to the previous reporting requirements in order to simplify them.
In 2020/2021, 51,211 injuries to employees were reported under RIDDOR.
Reporting of Injuries, Diseases and Dangerous Occurrances Regulations 2013 (hse.gov.uk)

## Slide 24: RIDDOR
RIDDOR applies to every workplace and puts duties on employers, the self-employed and people in control of work premises (the ‘responsible person’) to report and keep records of:
  work-related accidents which cause death or serious injuries (reportable injuries)
  certain ‘dangerous occurrences’ (incidents with the potential to cause harm)
  diagnosed cases of certain industrial diseases.
  Reporting of Injuries, Diseases and Dangerous Occurrences Regulations 2013 (legislation.gov.uk)

## Slide 25: COSHH
COSHH is a set of regulations put in place to protect workers from ill health when working with specific substances and materials. Training is provided where necessary. A breach of COSHH by an employer or employee is a crime, punishable by an unlimited fine. The regulations:
  protect against illness caused by hazardous substances
  help to prevent, control and monitor exposure to hazardous substances
  stipulate the risk assessment of working practices
  describe precautions.
  Control of Substances Hazardous to Health Regulations 2002 (legislation.gov.uk)

## Slide 26: Health and safety culture
An organisation’s culture can have as big an influence on safety outcomes as the safety management system. ‘Safety culture’ is a subset of the overall company culture.
In Organising for Safety (1993) the HSE described safety culture as:
the product of individual and group values, attitudes, perceptions, competencies, and patterns of behaviour that determine the commitment to, and the style and proficiency of, an organisation’s health and safety management. Organisations with a positive safety culture are characterised by communications founded on mutual trust, shared perceptions of the importance of safety and by confidence in the efficacy of preventive measures.

## Slide 27: Health and safety training and information
Regular training is a key aspect of maintaining and fostering a health and safety culture. It ensures all employees understand the health and safety requirements of their workplace and how to work safely and without risk to their health.
To maintain a health and safetty culture, all organisations should ensure that health and safety information is easily available in the workplace.
A further source of information is of course the HSE: https://hse.gov.uk/.
Notes: Shutterstock Item ID: 1809693421

## Slide 28: Recap
In this session we have covered the key pieces of legislation that govern the engineering and manufacturing industries. You do not need to know every detail of the law, but it is important that you clearly understand:
the main requirements of the key legislation
how to access the regulations
how the legislation affects your activities in the workplace, and how it keeps you safe
who is responsible for compliance with the legislation
how a ‘safety culture’ and regular training can protect everyone’s health and safety in the workplace.

## Slide 29
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.