## Slide 1: PowerPoint 5: Risk assessment
PowerPoint presentation
12. Health and safety principles and coverage
12.4 Risk assessment

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
explain why risk assessments are required and how they are conducted
understand the methods used for identifying hazards
be able to carry out a simple risk assessment
list and explain the hierarchy of controls.

## Slide 3: Risk assessment
A risk assessment must be completed:
  to back up a manufacturer’s data sheet for the Control of Substances Hazardous to Health Regulations (COSHH)
  to assess various activities carried out by employees.
  As an engineer, you must assess the risk to yourself and others when work is being carried out. This is at the heart of working safely.
After a risk assessment has been completed it will, as a minimum, result in the use of personal protective equipment (PPE) as required, and the presence of a first-aid kit. However, the more risk that is identified in the risk assessment, the more mitigation processes need to be put in place to protect the operative and anyone else who may be affected by the work being completed.

## Slide 4: Risk assessment
Key definitions
Accident: an unplanned, undesired occurrence which may result in harm or loss.
Hazard: anything that has the potential to cause loss or harm.
Risk: how likely it is that a hazard will actually cause harm or loss.
When a risk assessment is put together, you have to identify the work hazard and calculate the likelihood of an accident happening. Therefore, identifying the risk rating is important.

## Slide 5: Stages of risk assessment
hazard identification (HAZID)
hazard and operability study (HAZOP)
evaluation of risks (likelihood, severity, number of people affected)
implementation of control measures (hierarchy of controls)
recording the findings
reviewing and revising as necessary.
The Management of Health and Safety at Work Regulations (MHSWR) legally require employers to make decisions about the hazards, significant or not, faced in the workplace. The stages of risk assessment are hazard, risk and control, and comprise:

## Slide 6: Hazard identification (HAZID)
HAZID is the first stage in risk analysis used to identify potential causes of harm.
Equipment and tools: manual handling, machinery safeguarding, noise, vibration.
Stored energy: risk of electrical shock through non-isolated equipment.
Electricity: risk of electrocution.
Harmful substances, including gases: metalworking fluids, degreasing solvents, dust or fumes from welding, brazing, soldering, coating and painting.
Environment: working and storage areas, workplace order and cleanliness.

## Slide 7: Hazard and operability study (HAZOP)
HAZOP is a structured and systematic technique for risk management. It is used to identify and evaluate potential safety hazards in an organisation.
Risk identification
Risk assessment
Risk management
Risk
review

## Slide 8: Likelihood
By analysing the consequence and likelihood of a hazard, a rating score can be produced. The scores for the likelihood and consequences are multiplied to produce a total risk score. This is then read on a risk matrix.
Likelihood is scored as follows.
Likelihood |  |  |  |  | 
Score | 1 | 2 | 3 | 4 | 5
Description | Rare | Unlikely | Possible | Likely | Almost certain

## Slide 9: Consequence
Consequence is scored as follows.
Consequence |  |  |  |  | 
Score | 1 | 2 | 3 | 4 | 5
Description | Insignificant | Minor | Moderate | Major | Catastrophic
Example | Minor injury, no first aid | Harmful injury, first aid required, up to 3 days off work | Serious injury, medical assistance required. Injury must be reported | Major injury, urgent medical assistance required | Fatality

## Slide 10: Risk matrix
A risk matrix is used to define the level of risk by considering the probability of an incident. There are four risk levels: low (green), medium-low (yellow), medium-high (orange) and high (red).
Consequences/Impact | Catastrophic | 5 | 5 | 10 | 15 | 20 | 25
 | Major | 4 | 4 | 8 | 12 | 16 | 20
 | Moderate | 3 | 3 | 6 | 9 | 12 | 15
 | Minor | 2 | 2 | 4 | 6 | 8 | 10
 | Insignificant | 1 | 1 | 2 | 3 | 4 | 5
 |  |  | 1 | 2 | 3 | 4 | 5
 |  |  | Rare | Unlikely | Possible | Likely | Almost certain
Likelihood/Probability |  |  |  |  |  |  | 
Consequence/impact | Catastrophic | 5 | 5 | 10 | 15 | 20 | 25
 | Major | 4 | 4 | 8 | 12 | 16 | 20
 | Moderate | 3 | 3 | 6 | 9 | 12 | 15
 | Minor | 2 | 2 | 4 | 6 | 8 | 10
 | Insignificant | 1 | 1 | 2 | 3 | 4 | 5
 |  |  | 1 | 2 | 3 | 4 | 5
 |  |  | Rare | Unlikely | Possible | Likely | Almost certain
Likelihood/probability |  |  |  |  |  |  | 

## Slide 11: Document example
Pillar drill

## Slide 12: Control measures in engineering
Typical control measures used in engineering include:
machine guarding
machine isolation
PPE
eye protection
safety shoes
ear protection
gauntlets
helmets.

## Slide 13: Hierarchy of controls
The controls at the top of the pyramid are more effective and protective than those at the bottom.
Elimination
Reduction/substitution
Isolation
Engineering controls
PPE
Administration controls

## Slide 14: Controls in detail
Elimination: physical removal of a hazard, eg removal of any dangerous chemicals or machinery from a process.
Reduction/substitution: replacment of a hazard with something less hazardous, eg use of a less flammable substance in a process.
Isolation: isolation of machinery to protect people from the hazard, eg keeping a machine in a closed room and operating it remotely.
Engineering controls: use of machine guards to protect users.
Administration controls: changing the way people work by training them to use machinery safely.
PPE: protecting workers by using eye protection, safety shoes, ear protection, gauntlets, helmets etc.
Notes: Image source: https://en.wikipedia.org/wiki/Hierarchy_of_hazard_controls#/media/File:NIOSH%E2%80%99s_%E2%80%9CHierarchy_of_Controls_infographic%E2%80%9D_as_SVG.svg. Public domain

## Slide 15: Pause to discuss: control measures
Discuss in small groups what control measures may be needed for a new computer numerical control (CNC) machine being installed in the workplace.
What control measures are needed to protect the users and the environment?
Notes: Learners could be directed to the HSE advice: HSE COSHH MW1

## Slide 16
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.