## Slide 1: PowerPoint 6: Safe systems
PowerPoint presentation
12. Health and safety principles and coverage
12.5 Health and safety considerations in specific engineering contexts

## Slide 2: Objectives
PowerPoint presentation
By the end of this session, learners should be able to:
describe different health and safety hazards and risks, along with their associated safe systems, as appropriate to a range of engineering contexts.

## Slide 3: Safe systems
PowerPoint presentation
A safe system of work is a procedure to eliminate the risks that are involved in a specific operation. The priority of a safe system of work is to eliminate any risks involved.
Following a risk assessment process can reduce risks on site and ensure safe systems of work.
It is vital that safe systems and practices are adhered to so that everyone is working to the same high safety standards at all times.
Without these systems in place, accidents might occur that could cause injury or death.

## Slide 4: Safe systems
Hazard | Possible risks | Possible safe system
Mechanical equipment (such as metal guillotines, power presses, angle grinders) | Hands and fingers may be cut, sprained, dislocated, broken, crushed or severed Eye injuries can occur from flying metal fragments or shattered metal-grinding discs These injuries can result in permanent disability | Establish a maintenance programme to make sure all equipment is in safe working order Control mechanical hazards (eg by installing machine guarding) Train employees in safe operation of mechanical equipment Provide supervision Provide personal protective equipment (PPE) such as safety glasses and hearing protection where needed

## Slide 5: Safe systems
Hazard | Possible risks | Possible safe system
Welding | Electric shock, burns to eyes or body from the welding arc or hot metal surfaces Inhalation of fumes can result in nausea or serious illness | Provide adequate ventilation Provide PPE (welding mask or helmet with filtered lens, fire resistant gloves, leather apron, overalls, boots) Establish safe working procedures Provide appropriate training and supervision

## Slide 6: Safe systems
Hazard | Possible risks | Possible safe system
Hazardous substances (chemicals): paint, glue, solvents, gases for welding, cleaning liquids and powders | Irritation or burning of skin, or if fumes are breathed in Some chemicals, metal fumes and gases are flammable and exposure to a naked flame can result in a fire or explosion | Provide material safety data sheets (MSDS) Train workers in safety procedures Provide appropriate PPE: gloves, overalls, respirator, safety glasses and boots
Manual handling (bending, reaching, pulling, lifting) | Musculoskeletal disorders, including sprains and strains | Use mechanical aids to handle heavier items Use team lifts where required

## Slide 7: Safe systems
Hazard | Possible risks | Possible safe system
Foundries | Burns caused by hot metal surfaces Inhalation of fumes can result in nausea or serious illness | Provide adequate ventilation Provide PPE (welding mask or helmet with filtered lens, fire resistant gloves, leather apron, overalls, boots) Establish safe working procedures Provide appropriate training and supervision
Forklifts | Falls from height where people have been raised by forklifts Collisions with pedestrians | Ensure that all forklift operators have a current forklift licence Separate forklift pathways from pedestrian traffic

## Slide 8: Safe systems
Hazard | Possible risks | Possible safe system
Electricity and high voltage | Electric shock, electrocution | Ensure equipment is regularly inspected, tested and tagged Lock out, tag out faulty equipment: eg DANGER – DO NOT USE
Fire | Sources of ignition include: lighting, naked flames, electrical equipment, anything that causes sparks or gets very hot | Identify fire hazards Identify people at risk Ensure all workers are trained to use equipment that uses heat or creates sparks

## Slide 9: Safe systems
Hazard | Possible risks | Possible safe system
Oxygen | Spontaneous fire from oxygen enrichment (where oxygen levels are greater than in the air) Use of materials not compatible with oxygen Leaking valves and hoses in poorly ventilated room | Keep oxygen equipment in good condition Ensure good ventilation Take great care when using oxygen

## Slide 10: Safe systems
Hazard | Possible risks | Possible safe system
Confined spaces | Asphyxiation due to toxic gas fumes or vapour Excessive heat Flammable substances and oxygen enrichment Becoming trapped | Adequate ventilation, purge gas from confined space PPE (welding mask or helmet with filtered lens, fire resistant gloves, leather apron, overalls, boots) Respiratory protective equipment (RPE) Provide cooling air to reduce excessive heat Remove all flammable substances Establish safe working procedures Provide appropriate training and supervision

## Slide 11: Permit to work
PowerPoint presentation
A permit to work (PTW) will sometimes be required in certain specialised, high-risk situations, examples of which are given on the next slide. In such circumstances, safety procedures are agreed in advance, and the permit authorises key people to carry out specific work within an agreed time frame.
The PTW should set out all the precautions needed, based on a risk assessment.
Permits to work - COSHH (hse.gov.uk)

## Slide 12: Permit to work
PowerPoint presentation
Examples of where a permit to work is required are:
  completing ‘hot works’, eg welding/plasma cutting
  working in confined spaces, eg, in a tank
  lone working, eg, in a sewer/tank
  maintaining machinery and equipment, eg maintenance of a disc cutter etc.

## Slide 13: Lock out, tag out (LOTO)
Lock out, tag out (LOTO) is a safety procedure used to ensure that dangerous machines are properly shut off and cannot be started again prior to the completion of maintenance or repair work.
The equipment is isolated and locked, and a tag is placed on the lock, identifying the worker who placed it.
The worker holds the key for the lock, ensuring that only they can remove the lock and start the machine. This prevents accidental startup of a machine which could be hazardous.

## Slide 14: Your turn
Consider the use of chemicals in your own workplace or place of study. This doesn’t have to be engineering related – for example, chemicals are used in many cleaning products, swimming pools and washrooms.
What procedures, if any, are in place for their use? Where are these chemicals stored when not in use? What PPE is worn, if any? What paperwork is associated with the chemicals used?
Notes: Image source Shutterstock

## Slide 15
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.