## Slide 1
15. Stock and asset management
15.1 Stock and inventory management principles and practices
PowerPoint 3: Stock practices in industry

## Slide 2: Objectives
By the end of this session, learners should be able to:
explain the stock/production practices of ‘just in time’ (JIT), made to stock (MTS), made to order (MTO) and material requirements planning (MRP)
describe the basic working of a supply chain
outline the importance of packaging as part of stock processes.

## Slide 3: Just in time (JIT)
  Just in time (JIT) is a very descriptive name for a stock and distribution practice that is guided by three things: what, when and how much.
  Toyota was the first to introduce the concept of JIT on a large scale.
Notes:   https://www.youtube.com/watch?v=cAUXHJBB5CM

## Slide 4: What is JIT?
Most companies create and hold inventory in excess, meaning they create goods in anticipation of orders.
JIT involves creating, storing and keeping track of only enough orders to supply the actual demand for the company’s products.
It is designed to be highly efficient and reduce waste and can hence be regarded as a lean manufacturing approach.
JIT
Reduce idle time
Improve
accuracy
Reduce waste
Improve
efficiency
Improve cash flow

## Slide 5: Advantages and disadvantages of JIT
Advantages | Disadvantages
Reduces inventory costs | No extra stock on hand to fill unexpected orders
Improves cash flow | Risk that surges in demand cannot be met and sales will be lost
Improves efficiency and accuracy of forecasting | Risk that a supply chain shock halts production
Reduces wasted time and materials | JIT requires skill and precision to implement effectively

## Slide 6: Made to stock (MTS)
  Made to stock (MTS) is a more traditional production technique in which producers make and store items on a large scale in anticipation of consumer demand. The quantities made can be based on a forecast of sales or on the sales history of a product.
  On the same principle, many types of industry make parts or assemblies that go together to make the final product (sub-assemblies). Clearly, if a company runs out of a part the whole factory can grind to a halt while more are made.
  If this is the case, the company may choose to make excess components. Sometimes a company may choose keep more ‘in stock’ in anticipation of an increase in orders.

## Slide 7: MTS example
  A company that makes chocolate treats will need to change a lot of its tooling in the factory to make Easter eggs instead of more traditional chocolate bars. The eggs are therefore made well in advance, in anticipation of almost guaranteed demand in certain countries.
  This is why Easter eggs might appear on the supermarket shelves just after Christmas.

## Slide 8: Your turn
Can you think of another example of products to which MTS might apply?
What are the advantages to manufacturers of this advance stocking practice?
What are the risks?

## Slide 9: Made to order (MTO)
  Made to order (MTO) is a stock/production strategy that allows consumers to purchase products that are customised to their specifications.
  It is a manufacturing process in which the production of an item begins only after a confirmed customer order is received. For example, a company making clothes for a customer such as a supermarket will make them to the supermarket’s specifications according to its order.
  MTO also applies on a very small, one-off scale. For example, every car ordered from Bentley is unique – it is MTO. The customer decides on the paint colour(s), upholstery, instruments, extra features and so on, and the car is made to their specification.

## Slide 10: Advantages and disadvantages of MTO
Advantages | Disadvantages
Allows customisation for customers | Increases costs
Reduces stock obsolescence | Increases wait times for finished product
Reduces finished goods inventory | 
Reduces waste | 

## Slide 11: Material requirements planning (MRP)
Material requirements planning (MRP) is a production, planning scheduling and inventory control system used to manage manufacturing processes. Many manufacturers use software to carry out MRP. An MRP system will be used to determine what to buy, in what quantities, and when.
MRP software is designed to:
Ensure raw materials are available for production and that products are available to deliver to customers.
Maintain the lowest possible material and product levels in stock.
Plan manufacturing activities, delivery schedules and purchasing.

## Slide 12: Advantages and disadvantages of MRP
Advantages | Disadvantages
Reliable: ensures materials and components are available when needed | Heavy reliance on input data being accurate – inaccurate data will produce inaccurate outcomes
Minimises inventory levels | High cost of software implementation
Reduces customer lead times, giving higher customer satisfaction | Lack of flexibility to respond to peaks/troughs in demand
Optimises inventory management | 

## Slide 13: Supply chains and stock movements
  Supply chain is the term used to describe how parts, components, materials and products ‘move’ from one company to another, and then on to the customer.
Company C
buys the bolts and packages them up with nuts and washers
Company B
uses the steel to make bolts
Company A
mines iron and makes steel
Company D
buys the bolts, nuts and washers and uses them to make shock absorbers
Company E
buys the shock absorbers for its mountain bikes
Company F
buys the shock absorbers and uses them in its quad bikes
Company G
buys the shock absorbers and sells them as spares in their shops

## Slide 14: Supply chain failure
  A failure anywhere is the supply chain will cause problems for all the companies further down the chain. If Company D has a flood, Companies E, F and G will have no shock absorbers to buy.
Company C
Company B
Company A
Company D
FLOODED

## Slide 15: Packaging
Packaging is an essential stock practice. Almost all manufactured items will need packaging. Packaging ensures that:
items are batched in sensible quantities per package and protected from damage
items can be stacked in containers strong enough to ensure none are crushed or damaged.
Packaged products need to be easily transportable (eg on suitable pallets) by hand, forklift, etc, so they can be loaded quickly and safely into different modes of transport (eg containers, road vehicles, trains, aeroplanes).

## Slide 16: Your turn
This laptop is made in China but can be delivered to your door by Amazon Prime the next day. How is this achieved?

## Slide 17
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.