## Slide 1
PowerPoint 5: Capacity management
15. Stock and asset management
15.2 Asset management and control principles.

## Slide 2: Objectives
By the end of this session, learners should be able to:
describe the advantages and disadvantages associated with methods of capacity management.

## Slide 3: What is capacity?
Capacity is the term used to describe the ability of available resources to meet a certain level of demand.
Resources = people, facilities, storage, equipment etc.
In a restaurant, capacity will be influenced by the number of tables and chairs, the size of the kitchen, the number of staff and the opening times.
In a production or manufacturing setting, capacity is influenced by the size of the production facility, the number of staff, the available equipment on the production line, storage facilities and available transportation.

## Slide 4: Capacity management
Managing production capacity means using people, machines and processes to best effect. Capacity management should ensure that a business maximises its output at all times and under all conditions to achieve maximum production efficiency.
Capacity management goes hand in hand with understanding customer demand. If a factory works at full capacity to produce mountain bikes all year round, but sales of mountain bikes drop during the winter, there will be excess bikes to store which will not be sold until the spring. This excess capacity will cost the company money. Production capacity should therefore be adjusted to match demand.

## Slide 5: Benefits of capacity management
Capacity management:
plans production cycles ahead of time, to maximise production efficiency
reduces costs: a company can identify parts of its business not optimised and remove any bottlenecks
manages inventory better and anticipates problems in the supply chain
allows better allocation of human and material resources
helps a business decide when it needs to expand or contract.

## Slide 6: Capacity management methods
Commonly used capacity management strategies include:
lead strategy
lag strategy
match strategy
dynamic strategy.

## Slide 7: Lead and lag strategies
Lag strategy means a business determines capacity and waits until there is an actual steady increase in demand. The business then raises production capability to meet that demand. This is a low risk strategy, but the business will lose the opportunity to sell more if demand goes up quickly, because increasing production takes time (creating a lag in the supply chain). In a lead strategy the business increases capacity ahead of actual demand. This is a high risk strategy because if actual demand does not rise, inventory storage costs will still be high and the risk of wastage increases.

## Slide 8: Match and dynamic strategies
A match strategy makes small adjustments to capacity in an attempt to match demand. When it is clear demand will rise, the company boosts production with small adjustments. If demand goes up quickly, the company can partially satisfy that demand. If demand falls, it will not suffer huge losses. However, the small adjustments made to meet increased demand in a match strategy may not be enough, and business will be lost to competitors.
A dynamic strategy relies on market trends to determine capacity. The business analyses sales forecast data and actual demand, and then makes adjustments to production in advance. This approach may decrease the risk of shortage or wastage of inventory.

## Slide 9: Manufacturing resource planning (MRP II)
In Session 3 you learned about material requirements planning (MRP) which focuses on managing inventory of stock.
Manufacturing resource planning (MRP II) evolved from MRP to look more widely at capacity, operational activity and financial planning.

## Slide 10: Uses of MRP II software
Plan manufacturing capacity.
Schedule machine capacity.
Control inventory.
Manage purchasing.
Carry out MRP.
Enable quality assurance.
Create master production schedules.
Control costs/accounting.
Forecast demand.

## Slide 11: MRP II

## Slide 12: Advantages and disadvantages of MRP II
Advantages | Disadvantages
Better control of inventories | Requires business change to implement
Improved scheduling | Expensive
Productive relationships with suppliers | Only as accurate as the data it uses
Improved design control | Limited flexibility to respond to short-term fluctuations
Better quality and quality control | Now being superseded by enterprise resource planning (ERP), which looks at the whole business, not just production
Reduced working capital needed as inventory is better controlled | 
Improved cash flow due to quicker deliveries | 

## Slide 13: Bottlenecks
A bottleneck is a stage in a process where limited capacity reduces the efficiency of the whole process (such as a supply chain). Like the neck of a bottle, the chain narrows and the flow is impeded.
Short-term bottlenecks are temporary and are not normally a significant problem (eg staff sickness).
Long-term bottlenecks are more problematic (eg a machine which is not efficient enough and creates long queues).
Bottlenecks almost always exist in production as there will always be steps which are more complex or take longer than others.

## Slide 14: Throughput bottleneck
A throughput bottleneck is illustrated here. The machine making 60 items an hour slows the whole process down.

## Slide 15: Bottleneck analysis
Bottleneck analysis (in this example for a machining process) focuses on four things.
Identifying the location where accumulation (‘backing up’) is occurring.
Evaluating the throughput (the rate of production in the process).
Assessing whether each machine is being used at full capacity.
Finding the machine with the high wait time.
Cause and effect (fishbone) diagrams can help to identify bottlenecks in a process.
Attention can then turn to how to ease the bottleneck.

## Slide 16: Solving and preventing bottlenecks
Once the cause of the bottleneck has been identified, solutions can be tailored to the problem at that stage of the process. A solution may lie in:
increasing staffing
implementing ways to reduce downtime
identifying and removing any ‘non-value’ tasks (ie redundant tasks that don’t add value).
Bottlenecks can be prevented by improving staff training, planning for extra capacity in the system or budgeting to upgrade equipment and machinery.

## Slide 17
Any questions?
‘T-LEVELS’ is a registered trade mark of the Department for Education. ‘T Level’ is a registered trade mark of the Institute for Apprenticeships and Technical Education.